## Slide 1: Assembly Programming

## Slide 2: Outline
Arithmetic Operations
  How to subtract, OR, clear a register
Control Instructions
  Conditional Branches, Jump Instruction
  Example
Code Templates
  IF, FOR, WHILE, DO WHILE
  Examples

## Slide 3: What can you do with ADD, AND and NOT?
Which is all our ALU can do!

## Slide 4: What can you do with ADD, AND and NOT
Add
And
Not
Subtract
Or
Clear a register
Copy from one register to another
Increment a register by n, -16<=n<=15
This is just enough for the LC-3 to be Turing-complete!

## Slide 5: Subtract
;SUB R1, R2, R3 ;instruction does not exist
; how to subtract
; r1 = r2 – r3;
NOT R3, R3 ;flip the bits of R3
ADD R3, R3, #1 ;add 1 to R3 ;now R3 is -R3
ADD R1, R2, R3

## Slide 6: OR
;OR R1, R2, R3 ;instruction does not exist
; how to do OR: use DeMorgan’s Law
; r1 = r2 | r3;
NOT R2, R2 ;R2 = ~R2
NOT R3, R3 ;R3 = ~R3
AND R1, R2, R3 ;R1 = ~R2 & ~R3
NOT R1, R1 ;R1 = ~(~R2 & ~R3)

## Slide 7: Other Operations
;CLR R1 ; instruction doesn’t exist
; r1 = 0;
AND R1, R1, #0
;MOV R1, R2 ; instruction doesn’t exist
; r1 = r2;
ADD R1, R2, #0

## Slide 8: Control Instructions
0000
n
z
p
PCoffset9
BR
1100
000
BaseR
000000
JMP
0100
1
PCoffset11
JSR
JSRR
0100
0
00
BaseR
000000
1000
000000000000
RTI
1111
0000
trapvect8
TRAP
1100
RET
000
111
000000

## Slide 9: Conditional Branch
0000
n
z
p
PCoffset9
BR

## Slide 10: What can we do with a BR?

## Slide 11: What can we do with a BR?
If then else
For
While
Do while
Conditional Branch
Unconditional branch (BRNZP or BR)
Never branch (NOP)

## Slide 12: JMP Instruction
1100
000
BaseR
000000
JMP

## Slide 13: What can we do with a JMP?

## Slide 14: What can we do with a JMP?
Go To!!!!
Branch long distances!!!
We will rarely use JMP in this class
BR is much more commonly used

## Slide 15: Differences Between BR & JMP
BRx
  Can branch on N, Z, and P conditions
  Can always branch (BR or BRnzp)
  Can never branch (NOP)
  Destination address is always PCoffset9
  Can’t branch more than -256 to 255 words
JMP
  Always branches
  Destination address always in a register
  Can branch to any memory address

## Slide 16: How do we do IF using a BR (branch)?
First do an operation to set the condition codes
Then BR with the appropriate combination of NZP conditions in the instruction

## Slide 17: Every Condition: Comparison with Zero
A < B
A-B < B-B
A-B < 0
N condition code
A == B
A-B == B-B
A-B == 0
Z condition code
A > B
A-B > B-B
A-B > 0
P condition code

## Slide 18: Condition Codes
  N Z P
  Think: < == >
  BR (branch conditions)
  < N
  <= NZ
  == Z
  != NP
  >= ZP
  > P
  Always NZP (we abbreviate BRnzp as just BR, branch always)
  Never (no condition codes), we use NOP (no operation)

## Slide 19: Stylized Assembly Coding
Assembly programming gives the programmer a LOT of freedom
  Freedom to optimize performance whether needed or not
  Freedom to write impossibly complex code
  Freedom to make a zillion different errors
  Freedom to debug everything in binary
Is this always a good idea?
  If you’re just learning
  If you don’t want to make a career of it
  If you recognize that a compiler/optimizer can do a better job
What if we taught you some conventions that allow you to write and understand code much more quickly? Would you use them?

## Slide 20: Our Suggested Convention: Act Like a Compiler
Write your algorithm in a high-level language
Write down where you are going to store your variables (register, static memory, stack offset, etc.)
  Use comments for registers and stack offsets
  Use assembler directives to reserve memory
Copy your algorithm with “;” at the beginning of each line to create assembly language comments

## Slide 21: Our Suggested Convention: Act Like a Compiler
Translate each statement into a stanza of the appropriate machine language instructions
  For complex statements, like IF, WHILE, CALL, use templates!
  Make sure that each stanza you translate is independent of your other stanzas
    At the start, don’t depend on the contents of temporary registers
    At the start, don’t depend on the condition codes
    At the end, store your modified values where they belong
This will NOT result in the most efficient code, but it will be correct code
  plus an optimizer could easily make it efficient by throwing out the unneeded instructions you write, so who cares?

## Slide 22: Example Program
Write a program to be located at address x3000 which will sum up 12 integers located in memory addresses x3100-x310B

## Slide 23: Sum a List of 12 Integers
M = x3100
S = 0
C = 12
C > 0
S = S + Mem[M]
M = M + 1
C = C - 1
YES
NO

## Slide 24: Write Some Pseudo-Code (or Java or C or …)
short Mem[65536];
int S = 0;
int M = x3100;
int C = 12;
while (C > 0) {
  S = S + Mem[M];
  C = C - 1;
  M = M + 1;
  }

## Slide 25: Turn Your Pseudo-Code Into Assembly Language Comments
; int S = 0;
; int M = x3100;
; int C = 12;
; while (C > 0) {
  ; S = S + Mem[M];
  ; C = C - 1;
  ; M = M + 1;
  ; }

## Slide 26: Decide Where Variables Will Be Stored
; S is R1, M is R2, C is R3
; int S = 0;
; int M = x3100;
; int C = 12;
; while (C > 0) {
  ; S = S + Mem[M];
  ; C = C - 1;
  ; M = M + 1;
  ; }

## Slide 27: int S = 0
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,#0
; int M = x3100;
; int C = 12;
; while (C > 0) {
  ; S = S + Mem[M];
  ; C = C - 1;
  ; M = M + 1;
  ; }

## Slide 28: int M = x3100
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,#0
; int M = x3100;
LD R2,MINIT
; int C = 12;
; while (C > 0) {
  ; S = S + Mem[M];
  ; C = C - 1;
  ; M = M + 1;
  ; }
  MINIT .fill x3100

## Slide 29: int C = 12
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,#0
; int M = x3100;
LD R2,MINIT
; int C = 12;
AND R3,R3,#0
ADD R3,R3,#12
; while (C > 0) {
  ; S = S + Mem[M];
  ; C = C - 1;
  ; M = M + 1;
  ; }
  MINIT .fill x3100

## Slide 30: while (C > 0) {
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,#0
; int M = x3100;
LD R2,MINIT
; int C = 12;
AND R3,R3,#0
ADD R3,R3,#12
; while (C > 0) {
W1 ADD R3,R3,#0
BRnz ENDW1
  ; S = S + Mem[M];
  ; C = C - 1;
  ; M = M + 1;
  ; }
  MINIT .fill x3100

## Slide 31: } (end of the while)
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,0
; int M = x3100;
LD R2,MINIT
; int C = 12;
AND R3,R3,#0
ADD R3,R3,12
; while (C > 0) {
W1 ADD R3,R3,#0
BRnz ENDW1
  ; S = S + Mem[M];
  ; C = C - 1;
  ; M = M + 1;
  ; }
  BR W1
  ENDW1
  MINIT .fill x3100

## Slide 32: S = S + Mem[M]
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,0
; int M = x3100;
LD R2,MINIT
; int C = 12;
AND R3,R3,#0
ADD R3,R3,12
; while (C > 0) {
W1 ADD R3,R3,#0
BRnz ENDW1
  ; S = S + Mem[M];
  LDR R4,R2,#0
  ADD R1,R1,R4
  ; C = C - 1;
  ; M = M + 1;
  ; }
  BR W1
  ENDW1
  MINIT .fill x3100

## Slide 33: C = C - 1
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,#0
; int M = x3100;
LD R2,MINIT
; int C = 12;
AND R3,R3,#0
ADD R3,R3,#12
; while (C > 0) {
W1 ADD R3,R3,#0
BRnz ENDW1
  ; S = S + Mem[M];
  LDR R4,R2,#0
  ADD R1,R1,R4
  ; C = C - 1;
  ADD R3,R3,#-1
  ; M = M + 1;
  ; }
  BR W1
  ENDW1
  MINIT .fill x3100

## Slide 34: M = M + 1
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,#0
; int M = x3100;
LD R2,MINIT
; int C = 12;
AND R3,R3,#0
ADD R3,R3,#12
; while (C > 0) {
W1 ADD R3,R3,#0
BRnz ENDW1
  ; S = S + Mem[M];
  LDR R4,R2,#0
  ADD R1,R1,R4
  ; C = C - 1;
  ADD R3,R3,#-1
  ; M = M + 1;
  ADD R2,R2,#1
  ; }
  BR W1
  ENDW1
  MINIT .fill x3100

## Slide 35: Add a Little Window Dressing
.orig x3000
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,#0
; int M = x3100;
LD R2,MINIT
; int C = 12;
AND R3,R3,#0
ADD R3,R3,#12
; while (C > 0) {
W1 ADD R3,R3,#0
BRnz ENDW1
  ; S = S + Mem[M];
  LDR R4,R2,#0
  ADD R1,R1,R4
  ; C = C - 1;
  ADD R3,R3,#-1
  ; M = M + 1;
  ADD R2,R2,#1
  ; }
  BR W1
  ENDW1 HALT
  MINIT .fill x3100
  .end

## Slide 36: And Add Some Data
.orig x3100
.fill 3
.fill 4
.fill 5
.fill 1
.fill 6
.fill 2
.fill 7
.fill 8
.fill 9
.fill 12
.fill 10
.fill 11
.end

## Slide 37: Assembly Algorithm
Pass 1
  Start with lc (location counter) set to 0
  For each line in the program
    If there is a tag, add(tag, lc) to the symbol table
    Increment lc by the amount of memory the line takes up (often one word)
Pass 2
  Start with lc set to 0
  For each line in the program
    Look up any symbol in the line and replace it with its value in the symbol table. If it’s a PC-relative address, replace the symbol with its symbol table value – (lc + 1)
    Convert the opcode to 4-bits, registers to 3-bits, and immediate/offset values to the right number of bits for the opcode
    Output the assembled words into the object file
    Increment lc by the amount of memory the line takes up

## Slide 38: What Do We Get?
Memory
Our Code
Why the line?

## Slide 39: What Do We Get? Page 2
Memory
Our Code

## Slide 40: Question
NOP
ADD R3,R3,#0
BRNZ #-6
LDR R4,R2,#0
ST R0,#-256
How else does complex display the value x3100?
10

## Slide 41: Code Templates
Do you always have to write all the code from scratch?
Do you think the machine code for if/then is very similar each time you write it?
What about while, for, and do?
So why shouldn’t we make some templates instead of reinventing the wheel each time?
Using template will make your life easier

## Slide 42: if (R1>0) then .. else ..
ADD R1,R1,#0; if (R1>0) then
BRnz ELSE1
…[THEN part]…
BR ENDIF1
ELSE1 NOP ; else
…[ELSE part]…
ENDIF1 NOP ; endif

## Slide 43: While (R1>0)
WHILE1 ADD R1,R1,#0 ; while(R1>0)
BRnz ENDW1
…[WHILE body]…
BR WHILE1
ENDW1 NOP ; endwhile

## Slide 44: for (init; R1>0; reinit)
…[initialize loop]… ; for (init;
FOR1 ADD R1,R1,#0
BRnz ENDF1 ; R1>0;
…[FOR body]…
…[reinitialize]… ; reinit)
BR FOR1
ENDF1 NOP

## Slide 45: do … while (R1>0);
DO1 NOP ; do
…[DO WHILE body]…
ADD R1,R1,#0
BRp DO1 ; while(x)

## Slide 46: Question
ADD R1,R1,#0 BRN E1 AND R2,R2,#0 BR X1 E1 AND R2,R2,#0 ADD R2,R2,#5 X1 NOP
ADD R1,R1,#0 BRZP E1 AND R2,R2,#0 BR X1 E1 AND R2,R2,#0 ADD R2,R2,#5 X1 NOP
ADD R1,R1,#0 BRZP X1 ADD R2,R2,#0 BR E1 E1 AND R2,R2,#0 ADD R2,R2,#5 X1 NOP
ADD R1,R1,#0 BRZP E1 AND R2,R2,#0 BR X1 E1 ADD R2,R2,#5 X1 NOP
Implement the following statement in assembly language if R1<0 then R2=0 else R2=5
20

## Slide 47: if (A == 0 && B == 0)
; Go to ELSE part if either condition is false
LD R0,A BRnp ELSE2 LD R0,B BRnp ELSE2
; THEN code goes here
BR ENDIF2 ELSE2 NOP
; ELSE code goes here
ENDIF2 NOP

## Slide 48: Question
0
1
2
3
What is the minimum number of branch instructions required to implement the control structure “if (A == 0)” which includes no else part?
LDR R0,A
BRNP Z
; ”then part”
Z NOP
30

## Slide 49: if (A == 0 || B == 0)
; Trick: Negate the conditions, swap THEN/ELSE parts ; & implement like && -- thanks Mr. DeMorgan
LD R0,A BRz THEN3 LD R0,B BRz THEN3
; ELSE code goes here
BR ENDIF3 THEN3 NOP
; THEN code goes here
ENDIF3 NOP

## Slide 50: Example
if (a < b) {
m = 5;
} else {
m = a+1;
}

## Slide 51: Example: If – then – else
a .fill 1
b .fill 5
; if (a < b) {
; rewrite:if (a – b < 0)
LD R1,a
LD R2,b
NOT R2,R2
ADD R2,R2,#1
ADD R1,R1,R2
BRZP EL1
; m = 5;
AND R1,R1,#0
ADD R1,R1,#5
ST R1,m
BR EIF1
;} else {
EL1 NOP
; m = a+1;
LD R1,a
ADD R1,R1,#1
ST R1,m
;}
EIF1 NOP

## Slide 52: Example: For
for (I = 0; I < 10; I = I + 1) {
J = J + I;
}

## Slide 53: Example: For
I .blkw 1
J .fill 0
;for (I = 0; I < 10; I = I + 1) {
; init: I = 0
AND R1,R1,#0
ST R1,I
; test (I – 10 < 0)
FOR1 LD R1,I
ADD R1,R1,#-10
BRzp EFOR1
; J = J + I;
LD R1,I
LD R2,J
ADD R2,R2,R1
ST R2,J
; reinit I=I+1
LD R1,I
ADD R1,R1,#1
ST R1,I
;}
BR FOR1
EFOR1 NOP

## Slide 54: Example: Array Addressing
short a[5]; short q; short i = 3;
q = a[2]; q = a[i];
a[i] = q;
q = a[i];

## Slide 55: Example: Array addressing
; i is R3, q is R4
;short q; ;short a[5];
a .blkw 5
;short i = 3;
AND R3,R3,#0 ADD R3,R3,#3
;q = a[2];
LEA R0,a LDR R4,R0,#2
;q = a[i];
LEA R0,a ADD R0,R0,R3 LDR R4,R0,#0
;a[i] = q;
LEA R0,a ADD R0,R0,R3 STR R4,R0,#0
;q = a[i];
LD R0,aaddr ADD R0,R0,R3 LDR R4,R0,#0 . . . aaddr .fill a
a[0]
a[1]
a[2]
a[3]
a[4]
a
a+1
a+2
a+3
a+4
Addr Memory Word

## Slide 56: Example: For
short A[10];
for (I = 0; I < 10; I = I + 1) {
J = J + A[I];
}

## Slide 57: Example: For
I .blkw 1
J .fill 0
;short A[10];
A .blkw 10
;for (I = 0; I < 10; I = I + 1) {
; init: I = 0
AND R1,R1,#0
ST R1,I
; test (I – 10 < 0)
FOR1 LD R1,I
ADD R1,R1,#-10
BRzp EFOR1
; J = J + A[I];
LD R1,I
LEA R2,A
ADD R1,R1,R2 LDR R1,R1,#0
LD R2,J
ADD R2,R2,R1
ST R2,J
; reinit I=I+1
LD R1,I
ADD R1,R1,#1
ST R1,I
;}
BR FOR1
EFOR1 NOP

## Slide 58: Question
Addr M
-
Addr M
Val J
Addr M
Val J+1
Addr M[J+1]
Val J+1
Val M[J+1]
Val J+1
LDI R1,M LD R2,J ADD R1,R1,R2 ADD R1,R1,#1 LDR R1,R1,#0 ST R1,K
LEA R1,M LD R2,J ADD R1,R1,R2 LDR R1,R1,#0 ST R1,K
LD R1,M LD R2,J ADD R1,R1,R2 LDR R1,R1,#0 ST R1,K
LEA R1,M LD R2,J ADD R2,R2,#1 ADD R1,R1,R2 LDR R1,R1,#0 ST R1,K
Implement the following statement in assembly language K = M[J+1];
Val M[J+1]
Val J+1
R1
R2
40

## Slide 59: Example: Array Addressing
struct { short x, y; } b[6]; short q; short i = 3;
q = b[3].y; q = b[i].y;
q = b[i].x;

## Slide 60: Example: Array addressing
; i is R3, q is R4 ;short q; ;struct { ; short x, y; ; } b[6];
b .blkw 12
;short i = 3;
AND R3,R3,#0 ADD R3,R3,#3
;q = b[3].y;
LEA R0,b LDR R4,R0,#7
;q = b[i].y;
LEA R0,b ADD R0,R0,R3 ADD R0,R0,R3 LDR R4,R0,#1
;q = b[i].x;
LEA R0,b ADD R0,R0,R3 ADD R0,R0,R3 LDR R4,R0,#0
b[0].x
b[0].y
b[1].x
b[1].y
b[2].x
b[2].y
b[3].x
b[3].y
b[4].x
b[4].y
b[5].x
b[5].y
b
b+1
b+2
b+3
b+4
b+5
b+6
b+7
b+8
b+9
b+10
b+11
Addr Memory Word

## Slide 61: Templates for Indexing into an Array
Fetching ARRAY[I] (far away)
LD R1, AD ;R1 is address of ARRAY[0]
LD R2, I ;R2 is index number
ADD R1, R1, R2 ;R1 is address of ARRAY[I]
LDR R1, R1, #0 ;R1 is value of ARRAY[I]
BR SK ;Don’t execute the address
AD .fill ARRAY
SK NOP
Storing ARRAY[I] (far away)
LD R1, AD ;R1 is address of ARRAY[0]
LD R2, I ;R2 is index number
ADD R1, R1, R2 ;R1 is address of ARRAY[I]
STR R3, R1, #0 ;value of ARRAY[I] is R3
BR SK ;Don’t execute the address
AD .fill ARRAY
SK NOP
Fetching ARRAY[I] (nearby)
LEA R1, ARRAY ;R1 is address of ARRAY[0]
LD R2, I ;R2 is index number
ADD R1, R1, R2 ;R1 is address of ARRAY[I]
LDR R1, R1, #0 ;R1 is value of ARRAY[I]
Storing ARRAY[I] (nearby)
LEA R1, ARRAY ;R1 is address of ARRAY[0]
LD R2, I ;R2 is index number
ADD R1, R1, R2 ;R1 is address of ARRAY[I]
STR R3, R1, #0 ;value of ARRAY[I] is R3

## Slide 62: Questions?

## Slide 63
0001
DR
SR1
0
00
SR2
ADD+
0101
DR
SR1
0
00
SR2
AND+
0001
DR
SR1
1
imm5
ADD+
0101
DR
SR1
1
imm5
AND+
0000
n
z
p
PCoffset9
BR
1100
000
BaseR
000000
JMP
0100
1
PCoffset11
JSR
JSRR
0100
0
00
BaseR
000000
LD+
0010
PCoffset9
DR
LDI+
1010
PCoffset9
DR
+ Indicates instructions that modify condition codes

## Slide 64
1000
000000000000
RTI
1111
0000
trapvect8
TRAP
offset6
0110
DR
LDR+
BaseR
PCoffset9
1110
LEA
DR
1001
111111
NOT+
DR
SR
1100
RET
000
111
000000
0011
SR
ST
PCoffset9
1011
STI
SR
PCoffset9
0111
BaseR
STR
SR
offset6
1101
reserved
+ Indicates instructions that modify condition codes