## Slide 1: The Stack and Subroutines

## Slide 2: Outline
Subroutines - overview
The Stack
LC-3 calling convention
  Stack Pointer and Frame Pointer
  Caller and Callee
  Examples

## Slide 3: Why do we have subroutines?
All of the following are related to subroutines:
  Methods
  Functions
  Procedures
We call them “subroutines” in assembly.
Fundamentally, subroutines are about reusing code

## Slide 4: Code That We Might Want to Reuse

## Slide 5: Reusing Code by Repeating

## Slide 6: Turn Into a Subroutine

## Slide 7: Using A Subroutine Call

## Slide 8: Call/Return Mechanism
0100
1
PCoffset11
JSR
JSRR
0100
0
00
BaseR
000000
1100
RET
000
111
000000

## Slide 9: What does JSR do?
R7 <- PC
PC <- PC + PCOffset11
(remember, PC has been incremented in the Fetch cycle)
0100
1
PCoffset11
JSR

## Slide 10: What does JSRR do?
R7 <- PC
PC <- BaseR
JSRR
0100
0
00
BaseR
000000

## Slide 11: What does RET do?
1100
RET
000
111
000000

## Slide 12: What does RET do?
Jumps to R7
1100
RET
000
111
000000

## Slide 13: Short and Long Reach Subroutines
jsr sub
sub xxx xxx xxx
...
...
...
ret
ld R2, far
jsrr r2
far .fill sub
...
...
sub xxx xxx xxx
ret

## Slide 14: Question
JSR
JSRR
JMP
BR
Today’s number is 78,423
The RET instruction has the same opcode as
10

## Slide 15: How do we write a subroutine?
What issues do we need to consider?

## Slide 16: Issue 1: What if our subroutine calls another subroutine?
What is R7 used for?
What happens to R7 if our subroutine calls another subroutine?

## Slide 17: Preserve the Return Address (R7)
We’d better find a way for our subroutine to save its R7 return address somewhere.
That way, we are safe to call another subroutine.
Then, we can restore our original R7, and know where to return to when we are done.

## Slide 18: Issue 2: we only have a few registers
With only 8 registers (R0-R7)
  We are going to quickly run out of registers to use.
Our main program is using some registers
  Our subroutine also needs to use some registers
  So let’s save the old values from the registers we’ll use
  And then we can “borrow” these registers to use our subroutine
  When we’re done, we’ll put back the original values into those registers – like they were never changed!

## Slide 19: Saving Registers in a Subroutine
; Subroutine that needs to use r1, r2 and r3
subr st r1, r1save
st r2, r2save
st r3, r3save
; work is done here
ld r1, r1save
ld r2, r2save
ld r3, r3save
ret
r1save .fill 0
r2save .fill 0
r3save .fill 0
See any problems?

## Slide 20: But wait !
How much memory space is lost if every subroutine declares space to save registers?
What happens if our subroutine calls itself?
  Recursion
  We’ll step on the saved registers in memory, and lose those values.

## Slide 21: Make It Bulletproof!
What do we need to save?
  Old values in the registers we will use
  Our return address (from R7)
Where should we save these values?

## Slide 22: How do we do it?
We can’t always save things in the same place
  E.g. a fixed memory location
So what kind of data structure might we use?
  Answer: a stack

## Slide 23: What is a Stack?
Stack
  Last in/First Out
  Supports two operations: Push/Pop

## Slide 24: How do we implement the stack?
Stack is located in some designated area of memory
We need to store the address of the top of the stack somewhere.
The stack could "grow" in either direction (up or down)

## Slide 25: Top of the stack
We only need to keep track of one thing:
  The “top” of the stack (TOS)
  The memory location where the last value was pushed onto the stack
  Which is also the next thing to pop off the stack
Let’s use R6 to store the “stack pointer”
  The top of the stack

## Slide 26: Where Do We Put the Stack?
Turns out there’s a convenient spot for the stack on the LC-3
Since the heap* grows up, let the stack grow down to lower memory addresses!
Note the memory address are listed low to high on the page; down is high to low, so the arrow appears to point up!
Code
Heap
Stack
* We’ll tell you what the heap is later, when we get into C programming.
R6

## Slide 27: A Software Stack Convention
Implemented in memory
  The Top Of Stack moves as new data is entered
    Here R6 is the Stack Pointer, a pointer to the Top Of Stack
  Note that “down” is again “up” on this page…

## Slide 28: Push & Pop
Push
  Decrement stack pointer (our stack is growing down to lower memory addresses)
  Then write data in R0 to new TOS
Pop
  Read data at current TOS into R0
  Then increment stack pointer
PUSH ADD R6, R6, # -1
STR R0, R6, # 0
POP LDR R0, R6, # 0
ADD R6, R6, # 1

## Slide 29: Running out of memory
What if stack is already full or empty?
  Before pushing, we could test for overflow
  Before popping, we could test for underflow
In this class, we’ll ignore bounds checking
  In the real world, it definitely needs to happen
What happens when the stack pointer runs into the heap?
  What do you call that?
  Hint: a popular website

## Slide 30: Question
Decrement R7 Store R0 at the address in R7
Store R0 at the address in R6 Decrement R6
Store R0 at the address in R7 Increment R7
Decrement R6 Store R0 at the address in R6
How do we push a word in R0 onto the LC-3 stack?
20
Today's number: 63,636

## Slide 31: How does a stack help with subroutines?
We can push R7 onto the stack – to save the return address
We can push each of the registers onto the stack, to save copies of their old values
  Then we can borrow those registers to re-use inside of our subroutine
When our subroutine is done, we just pop the return address and original registers back off the stack

## Slide 32: What else might a subroutine need to know, or store?
We’re already going to save on the stack:
  R7 (return address)
  Copies of registers
What other data does a subroutine use or need?
What else might we want to store on the stack?
  Arguments
  Return Value
  Local variables

## Slide 33: Stack Frame
All of the data on the stack, relevant to our subroutine
  Arguments
  Return Value
  Local Variables
  Saved Return Address (R7)
  Saved Registers

## Slide 34: A subroutine stack frame
int foo(int x, int y, int z){
int temp;
temp = x + y + z;
return temp;
}
3 arguments
1 local variable
return value
saved return address (R7)

## Slide 35: Stack Frame
Local variable: temp
Return Address
Return Value
Arg1: x
Arg2: y
Arg3: z
R6: SP
0000
FFFF
Where is x?
At SP+3

## Slide 36: WAIT!
Are we always sure where x is?
Is it always at R6+3?
  R6 is the stack pointer (SP)

## Slide 37: What If foo Looked Like This?
int foo(int x, int y, int z) {
int temp;
int arr[z];
...
x = 1;
...
}

## Slide 38: What If foo Looked Like This?
int foo(int x, int y, int z) {
int temp;
int arr[z];
...
x = 1;
...
}

## Slide 39: The New Picture
(z)
More of array arr… (unknown size, z)
Local variable: arr
Local variable: temp
Return Address
Return Value
Arg1: x
Arg2: y
Arg3: z
R6: SP
0000
FFFF
Where is x now?
(relative to R6)
?

## Slide 40: Solution: Frame Pointer!
Keep a “known” location in the stack frame in another register
Which register? R5
We’re going to ALWAYS point it to the first local variable
  (and we’ll always reserve space for at least one local var, even if we don’t have any local variables)
The frame pointer, R5, is an anchor
  At a predictable location in the stack frame

## Slide 41: The Frame Pointer, R5
(z)
More of array arr… (unknown size, z)
Local variable: arr
Local variable: temp
Return Address
Return Value
Arg1: x
Arg2: y
Arg3: z
R6: SP
0000
FFFF
Where is x now?
(relative to R5)
Always at a fixed offset after R5
?
R5: FP

## Slide 42: Special Purpose Registers
R0
R1
R2
R3
R4
R5 – Frame Pointer
R6 – Stack Pointer
R7 – Return Address
From now on (with subroutines),
  Only use R0-R4 as general purpose registers!

## Slide 43: LC-3 Stack Frame
Saved R4
Saved R3
Saved R2
Saved R1
Saved R0
[ additional local variables ]
Local variable 1
Old Frame Pointer (old R5)
Return Address (old R7)
Return Value
Arg1
Arg2 …
R6: SP
0000
FFFF
R5: FP
Note that we will also save the old R5 Frame Pointer (from the caller)

## Slide 44: How do we organize the stack frame – for any subroutine?
Adopt a Calling Convention

## Slide 45: Fair Warning!
There are zillions of ways to write a calling convention
Calling conventions are intimately connected to an ISA
Each is difficult to get “right”.
Patt, et al. have picked one and have done it “right”.
If you try to re-invent it, you will make yourself a lot of extra trouble.
Use the Patt LC-3 calling convention we’ll teach you.

## Slide 46: Definition
The stack frame, also known as an activation record, is the collection of all data on the stack associated with one subprogram call.
The stack frame generally includes the following components:
  The return address
  Argument variables passed on the stack
  Local variables
  Saved copies of any registers modified by the subroutine that need to be restored
Source: http://www.cs.uwm.edu/classes/cs315/Bacon/Lecture/HTML/ch10s07.html

## Slide 47: Definitions
Caller
  The code that will call a subroutine, e.g.
  m = mult(a,b);
Callee
  The subroutine definition
  int mult(a,b) {
    return a*b
  }

## Slide 48: Caller
What do we do to call a subroutine?
  Push arguments (in reverse order)
  JSR
What do we do after the subroutine returns?
  Pop return value
  Pop the arguments

## Slide 49: Caller: mult(A,B)
SP-> | 
SP-> | arg1: A
 | arg2: B
SP-> | RV
 | arg1: A
 | arg2: B
Starting stack
Just before JSR
After mult returns
0000
⇑
⇓
FFFF
SP-> | 
Ending Stack

## Slide 50: Caller: mult(A,B)
SP-> | 
SP-> | arg1: A
 | arg2: B
SP-> | RV
 | arg1: A
 | arg2: B
Starting stack
Just before JSR
After mult returns
0000
⇑
⇓
FFFF
SP-> | 
Ending Stack
Note the symmetry: The stack ends up exactly like it started out. After we’re done with the subroutine.

## Slide 51: Caller: mult(A,B)
SP-> | 
SP-> | arg1: A
 | arg2: B
SP-> | RV
 | arg1: A
 | arg2: B
Starting stack
Just before JSR
After mult returns
0000
⇑
⇓
FFFF
SP-> | 
Ending Stack
Note the symmetry: The stack ends up exactly like it started out. After we’re done with the subroutine. Clean up your room when you are done!

## Slide 52: Question
The arguments have been popped off the stack
The stack pointer has the same value as it did before the call
The stack pointer is one less than its value before the call
The stack pointer contains the return value of the subroutine
At the moment a subroutine returns, what can we say about the stack?
30

## Slide 53: What the effect of JSR?
A subroutine effectively pushes its return value on the stack
That is what JSR looks like
  From the perspective of the caller

## Slide 54: Assembly: Caller of mult(a,b)
; let’s call mult
; M = mult(A,B);
; assume M, A, B, MULT are
; labels
; push arguments
; in reverse order
; push B
LD R1, B
ADD R6, R6, #-1
STR R1, R6, #0
; push A
LD R1, A
ADD R6, R6, #-1
STR R1, R6, #0
; call mult
JSR MULT
; after MULT returns
; pop the return value
LDR R1, R6, #0
ADD R6, R6, #1
; save the ret val in M
ST R1, M
; pop the two args, A and B
ADD R6, R6, #2

## Slide 55: Symmetry of Caller (stack frame)
; m = mult(a,b) ; caller’s perspective
LD R0, B ; push B
ADD R6, R6, -1
STR R0, R6, 0
LD R0, A ; push A
ADD R6, R6, -1
STR R0, R6, 0
JSR MULT ; call subroutine (e.g. push ret val)
LDR R0, R6, 0 ; pop return value
ADD R6, R6, 1
ST R0, M ; save return value at m
ADD R6, R6, 2 ; pop two arguments (A,B)
{

## Slide 56: Stack Frame - Callee
When a subroutine is called (stack buildup)
  Save some registers (callee-saved)
  Make room for local variables
Do the work of the subroutine
When procedure is about to return (stack teardown)
  Prepare return value
  Restore registers
  RET

## Slide 57: LC-3 Stack Frame
Saved R4
Saved R3
Saved R2
Saved R1
Saved R0
[ additional local variables ]
Local variable 1
Old Frame Pointer (old R5)
Return Address (old R7)
Return Value
Arg1
Arg2 …
R6: SP
0000
FFFF
R5: FP

## Slide 58: After Callee Teardown
SP-> | arg1
 | arg2
 | arg3
Just Before JSR
0000
⇑
⇓
FFFF

## Slide 59: After Callee Teardown
SP-> | arg1
 | arg2
 | arg3
SP-> | SRn
 | …
 | SR1
 | …
FP-> | Locals
 | OldFP
 | RA
 | RV
 | arg1
 | arg2
 | arg3
Just Before JSR
During Callee
0000
⇑
⇓
FFFF

## Slide 60: Stack Frame Progression
SP-> | arg1
 | arg2
 | arg3
SP-> | SRn
 | …
 | SR1
 | …
FP-> | Locals
 | OldFP
 | RA
 | RV
 | arg1
 | arg2
 | arg3
SP-> | RV
 | arg1
 | arg2
 | arg3
Just Before JSR
During Callee
Just After RET
0000
⇑
⇓
FFFF

## Slide 61: Stack Frame Progression
SP-> | SRn
 | …
 | SR1
 | …
FP-> | Locals
 | OldFP
 | RA
 | RV
 | arg1
 | arg2
 | arg3
SP-> | RV
 | arg1
 | arg2
 | arg3
During Callee
Just After RET
0000
⇑
⇓
FFFF
After Call is Done

## Slide 62: LC-3 Calling Convention
y = foo(a, b, c);
Caller: Push args onto stack right to left!
Caller: Jump to subroutine
Callee: Decrement SP to leave four slots (ret value, ret addr, old FP, local var)
Callee: Save copy of R7 (Ret Addr), and copy of R5 (Old FP)
Callee: Save Callee: Set R5 (frame pointer) to be R6 (stack pointer)
Callee: Allocate space (SP) for local variables & saved registers (R0-R4)
Callee: Save registers R0-R4 used by the function
Callee: Execute the code in the function
Callee: Save the Ret Val (at R5 + 3)
Callee: Restore saved registers (R0-R4)
Callee: Set SP to FP, to pop off local vars and saved registers
Callee: Restore the Ret Addr (to R7), and old Frame Pointer (to R5)
Callee: Pop off 3 words (ret addr, old FP, first local var)
Caller: Grab the Ret(urn) Val(ue)
Caller: Deallocate space for Ret Val and args

## Slide 63
ADD R6, R6, -4 ; Allocate space
STR R7, R6, 2 ; Save Ret Addr
STR R5, R6, 1 ; Save Old FP
ADD R5, R6, 0 ; Copy SP to FP
ADD R6, R6, -5 ; Make room for saved regs & l.v. 1-n
STR R0, R5, -1 ; Save R0
STR R1, R5, -2 ; Save R1
STR R2, R5, -3 ; Save R2
STR R3, R5, -4 ; Save R3
STR R4, R5, -5 ; Save R4
;====== DO WORK OF SUBROUTINE HERE =============
; Get return value into some register, e.g. R0
STR R0, R5, 3 ; save return value on stack
LDR R4, R5, -5 ; Restore R4
LDR R3, R5, -4 ; Restore R3
LDR R2, R5, -3 ; Restore R2
LDR R1, R5, -2 ; Restore R1
LDR R0, R5, -1 ; Restore R0
ADD R6, R5, 0 ; Restore SP
LDR R5, R6, 1 ; Restore FP
LDR R7, R6, 2 ; Restore RA
ADD R6, R6, 3 ; Pop RA,FP,1st local variable
RET
{
{
Symmetry of the Callee
And the Stack Frame

## Slide 64: Three Oddities
We always allocate space for no less than one local variable, even when we need none
The caller always pushes N words of arguments, but always pops N+1 words (which includes the Return Value)
Which means the callee pushes M words of stack frame, but pops M-1 to leave the Return Value on top of the stack

## Slide 65: How might the stack frame change?
Is the stack frame the same for every subroutine?
If you only have one local variable, your stack frame will always look like the prior examples.
If you have two or more local variables, you’ll need to allocate more space and move the saved register locations up – to make room for the additional local vars.

## Slide 66: Saving registers
You always save R7 and R5
  The old Return Address, and old Frame Pointer
Easy answer: always save R0-R4 on the stack frame
  The five general purpose registers.
Optional:
  If your subroutine only needs to use two registers (e.g. R1,R2), then you don’t have to save the other regs (R0, R3, R4)
  But you have to know which registers you’ll use first
  It is easier just to always save all five (R0-R4) in your stack frame

## Slide 67
SP(R6)-> | Saved Reg #N
 | …
 | Saved Reg #1
 | Local variable L
 | …
FP(R5)-> | Local variable 1
 | Old FP
 | Return address (RA)
 | Return value (RV)
 | arg 1
 | …
 | arg N
The stack frame when the callee starts doing work:
0000
FFFF
Item | Location
Lv L | FP-L-1
RA | FP+2
RV | FP+3
Arg N | FP+N+3

## Slide 68: Questions?

## Slide 69: There’s Code in the Next Slides
The upcoming slides have example code in them to implement the LC-3 calling convention for a subroutine.
Not only should you feel free to copy the code for your own programs, I strongly recommend that you copy this code.
Reinventing the wheel can cost you many hours. Avoid it.
Pay attention to the places you need to customize based on number of local variables, number of arguments, (and number of saved registers).

## Slide 70: Example: mult(a,b)
Presume you have a subroutine call
  m = mult(x, 3)
  (assume m and x are labels in the caller)
And elsewhere a subroutine definition
  int mult(int a, int b) {
    int answer = 0; while (a>0) {
    answer += b;
    a--; return answer; }
So how do we implement the subroutine, and the caller?

## Slide 71: Caller: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
Caller ; push arguments in reverse order
; mult(x,3)
Caller
0000
⇑
⇓
FFFF
Pointers | Value | Purpose | Base+Offset
SP-> |  |  | 

## Slide 72: Caller: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
Caller ; push arguments in reverse order
; mult(x,3)
Caller AND R0, R0, 0 ; push(3)
ADD R0, R0, 3
0000
⇑
⇓
FFFF
Pointers | Value | Purpose | Base+Offset
SP-> |  |  | 

## Slide 73: Caller: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
Caller ; push arguments in reverse order
; mult(x,3)
Caller AND R0, R0, 0 ; push(3)
ADD R0, R0, 3
ADD R6, R6, -1
0000
⇑
⇓
FFFF
Pointers | Value | Purpose | Base+Offset
SP-> |  |  | 

## Slide 74: Caller: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
Caller ; push arguments in reverse order
; mult(x,3)
Caller AND R0, R0, 0 ; push(3)
ADD R0, R0, 3
ADD R6, R6, -1
STR R0, R6, 0
0000
⇑
⇓
FFFF
Pointers | Value | Purpose | Base+Offset
SP-> | 3 | arg 2 (b) | 

## Slide 75: Caller: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
Caller ; push arguments in reverse order
; mult(x,3)
Caller AND R0, R0, 0 ; push(3)
ADD R0, R0, 3
ADD R6, R6, -1
STR R0, R6, 0
LD R0, X ; push(x)
0000
⇑
⇓
FFFF
Pointers | Value | Purpose | Base+Offset
SP-> | 3 | arg 2 (b) | 

## Slide 76: Caller: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
Caller ; push arguments in reverse order
; mult(x,3)
Caller AND R0, R0, 0 ; push(3)
ADD R0, R0, 3
ADD R6, R6, -1
STR R0, R6, 0
LD R0, X ; push(x)
ADD R6, R6, -1
0000
⇑
⇓
FFFF
Pointers | Value | Purpose | Base+Offset
SP-> |  |  | 
 | 3 | arg 2 (b) | 

## Slide 77: Caller: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
Caller ; push arguments in reverse order
; mult(x,3)
Caller AND R0, R0, 0 ; push(3)
ADD R0, R0, 3
ADD R6, R6, -1
STR R0, R6, 0
LD R0, X ; push(x)
ADD R6, R6, -1
STR R0, R6, 0
0000
⇑
⇓
FFFF
Pointers | Value | Purpose | Base+Offset
SP-> | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 

## Slide 78: Caller: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
Caller ; push arguments in reverse order
; mult(x,3)
Caller AND R0, R0, 0 ; push(3)
ADD R0, R0, 3
ADD R6, R6, -1
STR R0, R6, 0
LD R0, X ; push(x)
ADD R6, R6, -1
STR R0, R6, 0
JSR MULT ; mult(x,3)
0000
⇑
⇓
FFFF
Pointers | Value | Purpose | Base+Offset
SP-> | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 
And off we go to the address of mult()

## Slide 79: Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Callee – the subroutine itself
; First, lay out our stack frame!
0000
⇑
⇓
FFFF
Pointers | Value | Purpose | Base+Offset
SP-> | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 

## Slide 80: Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Callee – the subroutine itself
; First, lay out our stack frame!
; This is always the same for 2
; args, 1 local variable, and
; 5 saved registers
; For other counts, just adjust the
; amount of stack space as needed
0000
⇑
⇓
FFFF
Pointers | Value | Purpose | Base+Offset
 |  | Saved Reg 5 | 
 |  | Saved Reg 4 | 
 |  | Saved Reg 3 | 
 |  | Saved Reg 2 | 
 |  | Saved Reg 1 | 
 |  | Local Var (answer) | 
 |  | Old Frame Ptr | 
 |  | Old Ret Address | 
 |  | Return Value | 
SP-> | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 

## Slide 81: Stack Buildup -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
MULT
0000
⇑
⇓
FFFF
Pointers | Value | Purpose | Base+Offset
 |  | Saved Reg 5 | 
 |  | Saved Reg 4 | 
 |  | Saved Reg 3 | 
 |  | Saved Reg 2 | 
 |  | Saved Reg 1 | 
 |  | Local Var (answer) | 
 |  | Old Frame Ptr | 
 |  | Old Ret Address | 
 |  | Return Value | 
SP-> | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 

## Slide 82: Stack Buildup -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
MULT ADD R6, R6, -4 ; push 4 wds
; set rv later
0000
⇑
⇓
FFFF
Pointers | Value | Purpose | Base+Offset
 |  | Saved Reg 5 | 
 |  | Saved Reg 4 | 
 |  | Saved Reg 3 | 
 |  | Saved Reg 2 | 
 |  | Saved Reg 1 | 
SP-> | ??? | Local Var (answer) | 
 | ??? | Old Frame Ptr | 
 | ??? | Old Ret Address | 
 | ??? | Return Value | 
 | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 

## Slide 83: Stack Buildup -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
MULT ADD R6, R6, -4 ; push 4 wds
; set rv later
STR R7, R6, 2 ; save RA
0000
⇑
⇓
FFFF
Pointers | Value | Purpose | Base+Offset
 |  | Saved Reg 5 | 
 |  | Saved Reg 4 | 
 |  | Saved Reg 3 | 
 |  | Saved Reg 2 | 
 |  | Saved Reg 1 | 
SP-> | ??? | Local Var (answer) | 
 | ??? | Old Frame Ptr | 
 | old R7 | Old Ret Address | 
 | ??? | Return Value | 
 | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 

## Slide 84: Stack Buildup -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
MULT ADD R6, R6, -4 ; push 4 wds
; set rv later
STR R7, R6, 2 ; save RA
STR R5, R6, 1 ; save old FP
; set local var later
0000
⇑
⇓
FFFF
Pointers | Value | Purpose | Base+Offset
 |  | Saved Reg 5 | 
 |  | Saved Reg 4 | 
 |  | Saved Reg 3 | 
 |  | Saved Reg 2 | 
 |  | Saved Reg 1 | 
SP-> | ??? | Local Var (answer) | 
 | old R5 | Old Frame Ptr | 
 | old R7 | Old Ret Address | 
 | ??? | Return Value | 
 | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 

## Slide 85: Stack Buildup -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
MULT ADD R6, R6, -4 ; push 4 wds
; set rv later
STR R7, R6, 2 ; save RA
STR R5, R6, 1 ; save old FP
; set local var later
ADD R5, R6, 0 ; FP = SP
Pointers | Value | Purpose | Base+Offset
 |  | Saved Reg 5 | 
 |  | Saved Reg 4 | 
 |  | Saved Reg 3 | 
 |  | Saved Reg 2 | 
 |  | Saved Reg 1 | 
SP-> | ??? | Local Var (answer) | 
 | old R5 | Old Frame Ptr | 
 | old R7 | Old Ret Address | 
 | ??? | Return Value | 
 | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 
FP->
0000
⇑
⇓
FFFF

## Slide 86: Stack Buildup -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
MULT ADD R6, R6, -4 ; push 4 wds
; set rv later
STR R7, R6, 2 ; save RA
STR R5, R6, 1 ; save old FP
; set local var later
ADD R5, R6, 0 ; FP = SP
Pointers | Value | Purpose | Base+Offset
 |  | Saved Reg 5 | R5, -5
 |  | Saved Reg 4 | R5, -4
 |  | Saved Reg 3 | R5, -3
 |  | Saved Reg 2 | R5, -2
 |  | Saved Reg 1 | R5, -1
SP-> | ??? | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | ??? | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
FP->
0000
⇑
⇓
FFFF

## Slide 87: Stack Buildup -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
MULT ADD R6, R6, -4 ; push 4 wds
; set rv later
STR R7, R6, 2 ; save RA
STR R5, R6, 1 ; save old FP
; set local var later
ADD R5, R6, 0 ; FP = SP
ADD R6, R6, -5 ; push 5 words
Pointers | Value | Purpose | Base+Offset
SP-> |  | Saved Reg 5 | R5, -5
 |  | Saved Reg 4 | R5, -4
 |  | Saved Reg 3 | R5, -3
 |  | Saved Reg 2 | R5, -2
 |  | Saved Reg 1 | R5, -1
FP-> | ??? | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | ??? | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 88: Stack Buildup -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
MULT ADD R6, R6, -4 ; push 4 wds
; set rv later
STR R7, R6, 2 ; save RA
STR R5, R6, 1 ; save old FP
; set local var later
ADD R5, R6, 0 ; FP = SP
ADD R6, R6, -5 ; push 5 words
STR R0, R5, -1 ; save SR1
Pointers | Value | Purpose | Base+Offset
SP-> |  | Saved Reg 5 | R5, -5
 |  | Saved Reg 4 | R5, -4
 |  | Saved Reg 3 | R5, -3
 |  | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | ??? | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | ??? | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 89: Stack Buildup -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
MULT ADD R6, R6, -4 ; push 4 wds
; set rv later
STR R7, R6, 2 ; save RA
STR R5, R6, 1 ; save old FP
; set local var later
ADD R5, R6, 0 ; FP = SP
ADD R6, R6, -5 ; push 5 words
STR R0, R5, -1 ; save SR1
STR R1, R5, -2 ; save SR2
Pointers | Value | Purpose | Base+Offset
SP-> |  | Saved Reg 5 | R5, -5
 |  | Saved Reg 4 | R5, -4
 |  | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | ??? | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | ??? | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 90: Stack Buildup -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
MULT ADD R6, R6, -4 ; push 4 wds
; set rv later
STR R7, R6, 2 ; save RA
STR R5, R6, 1 ; save old FP
; set local var later
ADD R5, R6, 0 ; FP = SP
ADD R6, R6, -5 ; push 5 words
STR R0, R5, -1 ; save SR1
STR R1, R5, -2 ; save SR2
STR R2, R5, -3 ; save SR3
Pointers | Value | Purpose | Base+Offset
SP-> |  | Saved Reg 5 | R5, -5
 |  | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | ??? | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | ??? | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 91: Stack Buildup -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
MULT ADD R6, R6, -4 ; push 4 wds
; set rv later
STR R7, R6, 2 ; save RA
STR R5, R6, 1 ; save old FP
; set local var later
ADD R5, R6, 0 ; FP = SP
ADD R6, R6, -5 ; push 5 words
STR R0, R5, -1 ; save SR1
STR R1, R5, -2 ; save SR2
STR R2, R5, -3 ; save SR3
STR R3, R5, -4 ; save SR4
Pointers | Value | Purpose | Base+Offset
SP-> |  | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | ??? | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | ??? | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 92: Stack Buildup -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
MULT ADD R6, R6, -4 ; push 4 wds
; set rv later
STR R7, R6, 2 ; save RA
STR R5, R6, 1 ; save old FP
; set local var later
ADD R5, R6, 0 ; FP = SP
ADD R6, R6, -5 ; push 5 words
STR R0, R5, -1 ; save SR1
STR R1, R5, -2 ; save SR2
STR R2, R5, -3 ; save SR3
STR R3, R5, -4 ; save SR4
STR R4, R5, -5 ; save SR5
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | ??? | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | ??? | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF
What next?

## Slide 93: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finally – we can do the work of mult()
;int mult(int a, int b) {
;int answer = 0;
;while (a>0) {
;answer += b;
;a--;
;}
;return answer;
;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | ??? | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | ??? | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 94: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finally – we can do the work of mult()
;int mult(int a, int b) {
;int answer = 0;
AND R0, R0, #0 ;R0 = 0
;while (a>0) {
;answer += b;
;a--;
;}
;return answer;
;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | ??? | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | ??? | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 95: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finally – we can do the work of mult()
;int mult(int a, int b) {
;int answer = 0;
AND R0, R0, #0 ;R0 = 0
STR R0, R5, 0 ;answer = R0 ;while (a>0) {
;answer += b;
;a--;
;}
;return answer;
;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | 0 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | ??? | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 96: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finally – we can do the work of mult()
;int mult(int a, int b) {
;int answer = 0;
AND R0, R0, #0 ;R0 = 0
STR R0, R5, 0 ;answer = R0 ;while (a>0) {
W1 LDR R0, R5, 4 ;R0 = a
;answer += b;
;a--;
;}
;return answer;
;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | 0 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | ??? | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 97: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finally – we can do the work of mult()
;int mult(int a, int b) {
;int answer = 0;
AND R0, R0, #0 ;R0 = 0
STR R0, R5, 0 ;answer = R0 ;while (a>0) {
W1 LDR R0, R5, 4 ;R0 = a
BRnz END_W1
;answer += b;
;a--;
;}
;return answer;
;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | 0 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | ??? | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 98: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finally – we can do the work of mult()
;int mult(int a, int b) {
;int answer = 0;
AND R0, R0, #0 ;R0 = 0
STR R0, R5, 0 ;answer = R0 ;while (a>0) {
W1 LDR R0, R5, 4 ;R0 = a
BRnz END_W1
;answer += b;
;a--;
;}
BR W1 ;return answer;
;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | 0 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | ??? | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 99: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finally – we can do the work of mult()
;int mult(int a, int b) {
;int answer = 0;
AND R0, R0, #0 ;R0 = 0
STR R0, R5, 0 ;answer = R0 ;while (a>0) {
W1 LDR R0, R5, 4 ;R0 = a
BRnz END_W1
;answer += b;
;a--;
;}
BR W1 ;return answer;
END_W1 NOP ;placeholder
;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | 0 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | ??? | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF
After the loop, what value will be in answer (local variable)?

## Slide 100: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finally – we can do the work of mult()
;int mult(int a, int b) {
;int answer = 0;
AND R0, R0, #0 ;R0 = 0
STR R0, R5, 0 ;answer = R0 ;while (a>0) {
W1 LDR R0, R5, 4 ;R0 = a
BRnz END_W1
;answer += b;
;a--;
;}
BR W1 ;return answer;
END_W1 NOP ;placeholder
;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | x*3 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | ??? | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 101: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finally – we can do the work of mult()
;int mult(int a, int b) {
;int answer = 0;
AND R0, R0, #0 ;R0 = 0
STR R0, R5, 0 ;answer = R0 ;while (a>0) {
W1 LDR R0, R5, 4 ;R0 = a
BRnz END_W1
;answer += b;
;a--;
;}
BR W1 ;return answer;
END_W1 LDR R0, R5, 0 ;R0 = answer
;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | x*3 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | ??? | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 102: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finally – we can do the work of mult()
;int mult(int a, int b) {
;int answer = 0;
AND R0, R0, #0 ;R0 = 0
STR R0, R5, 0 ;answer = R0 ;while (a>0) {
W1 LDR R0, R5, 4 ;R0 = a
BRnz END_W1
;answer += b;
;a--;
;}
BR W1 ;return answer;
END_W1 LDR R0, R5, 0 ;R0 = answer
STR R0, R5, 3 ;set ret val to answer ;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | x*3 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | x*3 | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 103: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finish the body of the while loop
;while (a>0) {
W1 LDR R0, R5, 4 ;R0 = a
BRnz END_W1
;answer += b;
;a--;
BR W1 ;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | x*3 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | x*3 | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 104: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finish the body of the while loop
;while (a>0) {
W1 LDR R0, R5, 4 ;R0 = a
BRnz END_W1
;answer += b;
LDR R0, R5, 0 ;R0 = answer
;a--;
BR W1 ;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | x*3 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | x*3 | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 105: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finish the body of the while loop
;while (a>0) {
W1 LDR R0, R5, 4 ;R0 = a
BRnz END_W1
;answer += b;
LDR R0, R5, 0 ;R0 = answer
LDR R1, R5, 5 ;R1 = b
;a--;
BR W1 ;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | x*3 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | x*3 | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 106: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finish the body of the while loop
;while (a>0) {
W1 LDR R0, R5, 4 ;R0 = a
BRnz END_W1
;answer += b;
LDR R0, R5, 0 ;R0 = answer
LDR R1, R5, 5 ;R1 = b
ADD R0, R0, R1 ;R0 = answer+b
;a--;
BR W1 ;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | x*3 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | x*3 | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 107: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finish the body of the while loop
;while (a>0) {
W1 LDR R0, R5, 4 ;R0 = a
BRnz END_W1
;answer += b;
LDR R0, R5, 0 ;R0 = answer
LDR R1, R5, 5 ;R1 = b
ADD R0, R0, R1 ;R0 = answer+b
STR R0, R5, 0 ;answer = R0
;a--;
BR W1 ;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | x*3 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | x*3 | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 108: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finish the body of the while loop
;while (a>0) {
W1 LDR R0, R5, 4 ;R0 = a
BRnz END_W1
;answer += b;
LDR R0, R5, 0 ;R0 = answer
LDR R1, R5, 5 ;R1 = b
ADD R0, R0, R1 ;R0 = answer+b
STR R0, R5, 0 ;answer = R0
;a--;
LDR R0, R5, 4 ;R0 = a
BR W1 ;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | x*3 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | x*3 | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 109: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finish the body of the while loop
;while (a>0) {
W1 LDR R0, R5, 4 ;R0 = a
BRnz END_W1
;answer += b;
LDR R0, R5, 0 ;R0 = answer
LDR R1, R5, 5 ;R1 = b
ADD R0, R0, R1 ;R0 = answer+b
STR R0, R5, 0 ;answer = R0
;a--;
LDR R0, R5, 4 ;R0 = a
ADD R0, R0, #-1 ;R0 = a-1
BR W1 ;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | x*3 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | x*3 | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 110: Implementation -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Finish the body of the while loop
;while (a>0) {
W1 LDR R0, R5, 4 ;R0 = a
BRnz END_W1
;answer += b;
LDR R0, R5, 0 ;R0 = answer
LDR R1, R5, 5 ;R1 = b
ADD R0, R0, R1 ;R0 = answer+b
STR R0, R5, 0 ;answer = R0
;a--;
LDR R0, R5, 4 ;R0 = a
ADD R0, R0, #-1 ;R0 = a-1
STR R0, R5, 4 ;a = a-1
BR W1 ;}
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | x*3 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | x*3 | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF
What do we do next? (Are we ready to return?)

## Slide 111: Stack Teardown -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; We need to tear down the stack frame
LDR R4, R5, -5 ; restore R4
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | x*3 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | x*3 | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 112: Stack Teardown -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; We need to tear down the stack frame
LDR R4, R5, -5 ; restore R4
LDR R3, R5, -4 ; restore R3
LDR R2, R5, -3 ; restore R2
LDR R1, R5, -2 ; restore R1
LDR R0, R5, -1 ; restore R0
Pointers | Value | Purpose | Base+Offset
SP-> | old R4 | Saved Reg 5 | R5, -5
 | old R3 | Saved Reg 4 | R5, -4
 | old R2 | Saved Reg 3 | R5, -3
 | old R1 | Saved Reg 2 | R5, -2
 | old R0 | Saved Reg 1 | R5, -1
FP-> | x*3 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | x*3 | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF

## Slide 113: Stack Teardown -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; We need to tear down the stack frame
LDR R4, R5, -5 ; restore R4
LDR R3, R5, -4 ; restore R3
LDR R2, R5, -3 ; restore R2
LDR R1, R5, -2 ; restore R1
LDR R0, R5, -1 ; restore R0
ADD R6, R5, 0 ; pop saved regs,
; and local vars
Pointers | Value | Purpose | Base+Offset
 | old R4 |  | 
 | old R3 |  | 
 | old R2 |  | 
 | old R1 |  | 
 | old R0 |  | 
FP-> | x*3 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | x*3 | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF
SP->

## Slide 114: Stack Teardown -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; We need to tear down the stack frame
LDR R4, R5, -5 ; restore R4
LDR R3, R5, -4 ; restore R3
LDR R2, R5, -3 ; restore R2
LDR R1, R5, -2 ; restore R1
LDR R0, R5, -1 ; restore R0
ADD R6, R5, 0 ; pop saved regs,
; and local vars
LDR R7, R5, 2 ; R7 = ret addr
Pointers | Value | Purpose | Base+Offset
 | old R4 |  | 
 | old R3 |  | 
 | old R2 |  | 
 | old R1 |  | 
 | old R0 |  | 
FP-> | x*3 | Local Var (answer) | R5, 0
 | old R5 | Old Frame Ptr | R5, 1
 | old R7 | Old Ret Address | R5, 2
 | x*3 | Return Value | R5, 3
 | x | arg 1 (a) | R5, 4
 | 3 | arg 2 (b) | R5, 5
0000
⇑
⇓
FFFF
SP->

## Slide 115: Stack Teardown -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; We need to tear down the stack frame
LDR R4, R5, -5 ; restore R4
LDR R3, R5, -4 ; restore R3
LDR R2, R5, -3 ; restore R2
LDR R1, R5, -2 ; restore R1
LDR R0, R5, -1 ; restore R0
ADD R6, R5, 0 ; pop saved regs,
; and local vars
LDR R7, R5, 2 ; R7 = ret addr
LDR R5, R5, 1 ; FP = Old FP
Pointers | Value | Purpose | Base+Offset
 | old R4 |  | 
 | old R3 |  | 
 | old R2 |  | 
 | old R1 |  | 
 | old R0 |  | 
SP-> | x*3 | Local Var (answer) | 
 | old R5 | Old Frame Ptr | 
 | old R7 | Old Ret Address | 
 | x*3 | Return Value | 
 | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 
0000
⇑
⇓
FFFF

## Slide 116: Stack Teardown -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; We need to tear down the stack frame
LDR R4, R5, -5 ; restore R4
LDR R3, R5, -4 ; restore R3
LDR R2, R5, -3 ; restore R2
LDR R1, R5, -2 ; restore R1
LDR R0, R5, -1 ; restore R0
ADD R6, R5, 0 ; pop saved regs,
; and local vars
LDR R7, R5, 2 ; R7 = ret addr
LDR R5, R5, 1 ; FP = Old FP
ADD R6, R6, 3 ; pop 3 words
Pointers | Value | Purpose | Base+Offset
 | old R4 |  | 
 | old R3 |  | 
 | old R2 |  | 
 | old R1 |  | 
 | old R0 |  | 
 | x*3 |  | 
 | old R5 |  | 
 | old R7 |  | 
SP-> | x*3 | Return Value | 
 | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 
0000
⇑
⇓
FFFF
And now we’re finally ready to return!

## Slide 117: Stack Teardown -- Callee: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; We need to tear down the stack frame
LDR R4, R5, -5 ; restore R4
LDR R3, R5, -4 ; restore R3
LDR R2, R5, -3 ; restore R2
LDR R1, R5, -2 ; restore R1
LDR R0, R5, -1 ; restore R0
ADD R6, R5, 0 ; pop saved regs,
; and local vars
LDR R7, R5, 2 ; R7 = ret addr
LDR R5, R5, 1 ; FP = Old FP
ADD R6, R6, 3 ; pop 3 words
RET ; mult() is done!
Pointers | Value | Purpose | Base+Offset
 | old R4 |  | 
 | old R3 |  | 
 | old R2 |  | 
 | old R1 |  | 
 | old R0 |  | 
 | x*3 |  | 
 | old R5 |  | 
 | old R7 |  | 
SP-> | x*3 | Return Value | 
 | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 
0000
⇑
⇓
FFFF
Where do we go now?

## Slide 118: After JSR – Caller: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Back to the caller, after JSR
; m = mult(x,3);
; push(3)
; push(x)
JSR MULT ;call mult(x,3)
Pointers | Value | Purpose | Base+Offset
 | old R4 |  | 
 | old R3 |  | 
 | old R2 |  | 
 | old R1 |  | 
 | old R0 |  | 
 | x*3 |  | 
 | old R5 |  | 
 | old R7 |  | 
SP-> | x*3 | Return Value | 
 | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 
0000
⇑
⇓
FFFF
What’s changed since we left?
From the caller’s perspective: JSR appeared to push the return value onto the stack!

## Slide 119: After JSR – Caller: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Back to the caller, after JSR
; m = mult(x,3);
; push(3)
; push(x)
JSR MULT ;call mult(x,3)
;pop the return value off the stack
Pointers | Value | Purpose | Base+Offset
 | old R4 |  | 
 | old R3 |  | 
 | old R2 |  | 
 | old R1 |  | 
 | old R0 |  | 
 | x*3 |  | 
 | old R5 |  | 
 | old R7 |  | 
SP-> | x*3 | Return Value | 
 | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 
0000
⇑
⇓
FFFF

## Slide 120: After JSR – Caller: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Back to the caller, after JSR
; m = mult(x,3);
; push(3)
; push(x)
JSR MULT ;call mult(x,3)
;pop the return value off the stack
LDR R0, R6, 0 ;R0 = return value
Pointers | Value | Purpose | Base+Offset
 | old R4 |  | 
 | old R3 |  | 
 | old R2 |  | 
 | old R1 |  | 
 | old R0 |  | 
 | x*3 |  | 
 | old R5 |  | 
 | old R7 |  | 
SP-> | x*3 | Return Value | 
 | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 
0000
⇑
⇓
FFFF

## Slide 121: After JSR – Caller: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Back to the caller, after JSR
; m = mult(x,3);
; push(3)
; push(x)
JSR MULT ;call mult(x,3)
;pop the return value off the stack
LDR R0, R6, 0 ;R0 = return value
ADD R6, R6, 1
Pointers | Value | Purpose | Base+Offset
 | old R4 |  | 
 | old R3 |  | 
 | old R2 |  | 
 | old R1 |  | 
 | old R0 |  | 
 | x*3 |  | 
 | old R5 |  | 
 | old R7 |  | 
 | x*3 |  | 
SP-> | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 
0000
⇑
⇓
FFFF

## Slide 122: After JSR – Caller: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Back to the caller, after JSR
; m = mult(x,3);
; push(3)
; push(x)
JSR MULT ;call mult(x,3)
;pop the return value off the stack
LDR R0, R6, 0 ;R0 = return value
ADD R6, R6, 1
;save return value at label m
Pointers | Value | Purpose | Base+Offset
 | old R4 |  | 
 | old R3 |  | 
 | old R2 |  | 
 | old R1 |  | 
 | old R0 |  | 
 | x*3 |  | 
 | old R5 |  | 
 | old R7 |  | 
 | x*3 |  | 
SP-> | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 
0000
⇑
⇓
FFFF

## Slide 123: After JSR – Caller: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Back to the caller, after JSR
; m = mult(x,3);
; push(3)
; push(x)
JSR MULT ;call mult(x,3)
;pop the return value off the stack
LDR R0, R6, 0 ;R0 = return value
ADD R6, R6, 1
;save return value at label m
ST R0, m
Pointers | Value | Purpose | Base+Offset
 | old R4 |  | 
 | old R3 |  | 
 | old R2 |  | 
 | old R1 |  | 
 | old R0 |  | 
 | x*3 |  | 
 | old R5 |  | 
 | old R7 |  | 
 | x*3 |  | 
SP-> | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 
0000
⇑
⇓
FFFF

## Slide 124: After JSR – Caller: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Back to the caller, after JSR
; m = mult(x,3);
; push(3)
; push(x)
JSR MULT ;call mult(x,3)
;pop the return value off the stack
LDR R0, R6, 0 ;R0 = return value
ADD R6, R6, 1
;save return value at label m
ST R0, m
;pop the arguments off the stack
Pointers | Value | Purpose | Base+Offset
 | old R4 |  | 
 | old R3 |  | 
 | old R2 |  | 
 | old R1 |  | 
 | old R0 |  | 
 | x*3 |  | 
 | old R5 |  | 
 | old R7 |  | 
 | x*3 |  | 
SP-> | x | arg 1 (a) | 
 | 3 | arg 2 (b) | 
0000
⇑
⇓
FFFF

## Slide 125: After JSR – Caller: mult(int a, int b) (This example: 2 arguments, 1 local variable, 5 saved registers)
; Back to the caller, after JSR
; m = mult(x,3);
; push(3)
; push(x)
JSR MULT ;call mult(x,3)
;pop the return value off the stack
LDR R0, R6, 0 ;R0 = return value
ADD R6, R6, 1
;save return value at label m
ST R0, m
;pop the arguments off the stack
ADD R6, R6, 2
Pointers | Value | Purpose | Base+Offset
 | old R4 |  | 
 | old R3 |  | 
 | old R2 |  | 
 | old R1 |  | 
 | old R0 |  | 
 | x*3 |  | 
 | old R5 |  | 
 | old R7 |  | 
 | x*3 |  | 
 | x |  | 
 | 3 |  | 
SP-> |  |  | 
0000
⇑
⇓
FFFF
Now the stack frame is right back where we started!

## Slide 126: Question
Return address, Return value, Saved FP, local variables, saved R0-R4
Return value, Return address, Saved FP, local variables, saved R0-R4
Saved R0-R4, Local variables, Saved FP, Return address, Return value
Return value, Return address, Saved FP, saved R0-R4, local variables
In what order does a subroutine push items to create its stack frame?
40
Today's Number: 98,065​

## Slide 127: Review of Stack Frame, LC-3 Calling Convention

## Slide 128: LC-3 Calling Convention
y = foo(a, b, c);
Caller: Push args onto stack right to left!
Caller: Jump to subroutine
Callee: Decrement SP to leave four slots (ret value, ret addr, old FP, local var)
Callee: Save copy of R7 (Ret Addr), and copy of R5 (Old FP)
Callee: Save Callee: Set R5 (frame pointer) to be R6 (stack pointer)
Callee: Allocate space (SP) for local variables & saved registers (R0-R4)
Callee: Save registers R0-R4 used by the function
Callee: Execute the code in the function
Callee: Save the Ret Val (at R5 + 3)
Callee: Restore saved registers (R0-R4)
Callee: Set SP to FP, to pop off local vars and saved registers
Callee: Restore the Ret Addr (to R7), and old Frame Pointer (to R5)
Callee: Pop off 3 words (ret addr, old FP, first local var)
Caller: Grab the Ret(urn) Val(ue)
Caller: Deallocate space for Ret Val and args

## Slide 129
ADD R6, R6, -4 ; Allocate space
STR R7, R6, 2 ; Save Ret Addr
STR R5, R6, 1 ; Save Old FP
ADD R5, R6, 0 ; Copy SP to FP
ADD R6, R6, -5 ; Make room for saved regs & l.v. 1-n
STR R0, R5, -1 ; Save R0
STR R1, R5, -2 ; Save R1
STR R2, R5, -3 ; Save R2
STR R3, R5, -4 ; Save R3
STR R4, R5, -5 ; Save R4
;====== DO WORK OF SUBROUTINE HERE =============
; Get return value into some register, e.g. R0
STR R0, R5, 3 ; save return value on stack
LDR R4, R5, -5 ; Restore R4
LDR R3, R5, -4 ; Restore R3
LDR R2, R5, -3 ; Restore R2
LDR R1, R5, -2 ; Restore R1
LDR R0, R5, -1 ; Restore R0
ADD R6, R5, 0 ; Restore SP
LDR R5, R6, 1 ; Restore FP
LDR R7, R6, 2 ; Restore RA
ADD R6, R6, 3 ; Pop RA,FP,1st local variable
RET
{
{
Symmetry of the Callee
And the Stack Frame

## Slide 130: Question
Return value
Return address
Saved FP
First local variable
Last local variable
First saved register
On the LC-3, where does R5 point in the stack frame during the execution of a subroutine?
50

## Slide 131: Questions?
Subroutines - overview
The Stack
LC-3 calling convention
  Stack Pointer and Frame Pointer
  Caller and Callee
  Examples