## Slide 1: Input/Output

## Slide 2: Outline
I/O Basics
  Asynchronous vs. Synchronous
  Memory Mapped I/O vs. Special I/O Instrs.
  Interrupt Driven cs. Polling
  LC-3 Implementation of Memory Mapped I/O
Keyboard Input
Monitor Output
Full Implementation on LC-3

## Slide 3: Synchronicity
Asynchronous
  Electronic, mechanical and human speed
  Speed mismatch
  Handshaking: Ready bit
Synchronous
  Processor operation
  Certain kinds of high speed I/O

## Slide 4: Transfer Timing
I/O events generally happen much more slowly than CPU cycles.
Synchronous
  data supplied at a fixed, predictable rate
  CPU reads/writes every X cycles
Asynchronous
  data rate less predictable
  CPU must synchronize with device, so that it doesn’t miss data or write too quickly

## Slide 5: How do we do I/O?

## Slide 6: How we do I/O

## Slide 7: Two Methods of Doing I/O
Special I/O instructions
  Need an opcode
  Need to be general enough to work with devices that haven’t been invented yet
Memory-mapped I/O
  Steal part of the address space for device registers
  Operations done by reading/writing bits in the device registers
  (We’re going to concentrate on this method)

## Slide 8: Device Registers
Data registers: Used for the actual transfer of data i.e. character code
Status registers: Information the device is telling us
Control registers: Allows us to set changeable device characteristics
Device registers are often part of the i/o device itself

## Slide 9: Device Registers
Options
  May be memory mapped. That is the device register has a memory address
  May have special I/O instructions

## Slide 10: Memory Mapped vs. Special I/O Instructions
If device registers are located at valid memory addresses, how can we access them?
How can they be located at valid memory addresses?
"The very old PDP-8 (from DEC, light years ago—1965) is an example of a computer that used special I/O instructions."

## Slide 12: Interrupt-Driven vs. Polling
Two ways to handle I/O completion
Interrupt-driven
  Excuse me but I've just given you a character
Polling
  Has a character been typed?
  Has a character been typed?
  Has a character been typed?
  Has a character been typed?
  Has a character been typed?
  Has a character been typed?
  (We’ll start with this approach)

## Slide 13: Family Vacation!
Dad, Dad, are we there yet?
Not yet.
Dad, Dad, are we there yet?
Not yet.
Dad, Dad, are we there yet?
Not yet. (sigh)
……….
This is polling, right?
So what would the interrupt script sound like?
Dad, Dad, are we there yet?
No. Put your heads back, take a nap and I’ll wake you when we get there.
(long silence)
OK kids, wake up! We’re here!

## Slide 14: Our First Attempts at I/O
We’ll be working with asynchronous I/O instead of synchronous
We’re going to use memory mapped I/O instead of special I/O instructions
We’re going to use polling instead of interrupts

## Slide 15: LC-3 Address Space
x0000
xFDFF
xFE00 = 1111 1110 0000 0000
xFFFF
Device registers
How many?

## Slide 16: Keyboard Input
KBSR (xFE00)
  Only uses 1 bit. Why bit 15 instead of 0?
  Bit 15 is set when a character is available
KBDR (xFE02)
  Really only need 8 bits but 16 easier
  This location is read-only
  Reading clears KBSR
(There’s also an Interrupt Enable bit not shown in KBSR to indicate we want to be interrupted when KBSR[15] is set to 1, but we’re going to wait to discuss that)
data
rdy

## Slide 17: Memory Mapped Input
MDR
MAR
ADDRESS
CONTROL
LOGIC
MEMORY
KBSR
KBDR
INPUT
Gate
MDR
LD.MAR
R.W/READ
16
2
16
16
2
INMUX
LD.MDR
MEM.EN,
R.W
Can you build a circuit that does this?
If MAR == 0xFE00
INMUX=1
else if MAR == 0xFE02 INMUX=2
else
INMUX=0

## Slide 18
; Read characters from the keyboard until CTRL/Z
.orig x3000
ld r4, term
lea r2, buffer ; Initialize buffer pointer
start ldi r1, kbsrA ; See if a char is there
BRzp start
ldi r0, kbdrA ; get the character
str r0, r2, 0 ; Store it in buffer
not r0, r0 ; subtract R4-R0
add r0, r0, #1 ; to check for termination
add r0, r0, r4 ; char stored in R4
brZ quit
add r2, r2, 1 ; Increment buffer pointer
br start ; Do it again!
quit halt
term .fill x001A ; CTRL/Z
kbsrA .fill xfe00
kbdrA .fill xfe02
buffer .blkw x0100
.end

## Slide 19: Monitor Output
DSR (xFE04)
  Transferring a character to DDR clears DSR
  When monitor is finished processing a character it sets DSR bit 15
  "Please sir, may I have another?”
DDR (xFE06)
  Transfer character to this address to print it on the monitor
(There’s also an Interrupt Enable bit not shown in DSR to indicate we want to be interrupted when DSR[15] is set to 1, but we’re going to wait to discuss that)
rdy
data

## Slide 20
; Write the contents of a string to the display
.orig x3000
lea r2, buffer ; Initialize buffer ptr
start ldr r0, r2, 0 ; Get char into r0
brZ quit ; Terminate on null
wait ldi r3, dsrA ; Are we ready?
brZP wait
sti r0, ddrA ; Send R0 to monitor
add r2, r2, 1 ; Move buffer ptr over 1
br start
quit halt
dsrA .fill xfe04
ddrA .fill xfe06
buffer .stringz "Hello, World!"
.end

## Slide 21
The RDY bit in the KBSR is cleared
A byte is moved from KBDR to the designated CPU register
A and B
None of the above
Loading a value from the Keyboard Data Register (KBDR) into a CPU register causes the following to happen:
10
Today's number is 98,065

## Slide 22: Full Implementation of LC-3 Memory-Mapped I/O
Because of interrupt enable bits, status registers (KBSR/DSR) must be written, as well as read.

## Slide 23: Questions?
I/O Basics
  Asynchronous vs. Synchronous
  Memory Mapped I/O vs. Special I/O Instrs.
  Interrupt Driven cs. Polling
  LC-3 Implementation of Memory Mapped I/O
Keyboard Input
Monitor Output
Full Implementation on LC-3