## Slide 1: Interrupts, TRAPs, and Exceptions

## Slide 2: Outline
The Operating System Machine Layer
Program Discontinuities
  Interrupts
  TRAPs
  Exceptions

## Slide 3: Operating System Machine Layer
Operating Systems are about sharing resources and protecting users from themselves and others.
Certain operations require specialized knowledge and protection:
  Specific knowledge of I/O device registers and the sequence of operations needed to use them
  I/O and memory resources shared among multiple users/programs; a mistake could affect lots of other users/processes!
Not every programmer knows (or wants to know) this level of detail, so we abstract them in an Operating System Machine Layer
We transparently provide service to I/O devices and we notify user programs of unexpected situations
We provide service routines or system calls (as part of operating system) to safely and conveniently perform low-level, privileged operations

## Slide 4: Road Map

## Slide 5: What are Program Discontinuities
Interrupts
  An I/O device is reporting a completion or an error (e.g. “Read completed”)
TRAPs
  The program is calling a privileged operating system subroutine (e.g. “Read a line from a file”)
Exceptions
  Something unanticipated has happened
    Hardware error in the CPU or memory
    Program error (e.g. illegal opcode, divide by zero)

## Slide 6: Program Discontinuities
We combine the discussion of program discontinuities because they are all handled in very similar ways
  Save the state of the CPU
  Raise the CPU privilege level
  Call an operating system routine
  Restore the state of the CPU and the privilege level
  Resume the executing program where it left off
Does this resemble an unplanned subroutine call?
  (The microcode isn’t subject to program discontinuities; its job is to provide that abstraction for the machine language program)
Properties
  Synchronous with the program (TRAPs and some exceptions) or asynchronous (interrupts and other exceptions)
  Anticipated by the programmer (TRAPs) or unanticipated (interrupts and exceptions)

## Slide 7: Interrupts
What are they?
Why do they exist?
Generation of Interrupt Signal
  Device
  Priority
  FSM Mods

## Slide 8: What are they?
Modifications to the hardware of the datapath and I/O system and additional software to allow an external device to cause the CPU to stop current execution and execute a "service" routine and then resume execution of the original program. Hence, an interrupt.
Remember the INT signal that the LC-3 microsequencer can test? That signal is what an interrupt ultimately needs to raise.

## Slide 9: Why Do They Exist?
Interrupts can be significantly more efficient than polling and are especially useful in an environment where there are numerous devices and multiple concurrent activities
Polling on the other hand is appropriate where there is a high likelihood of quick success or the CPU has nothing better to do
An interrupt is an unscripted subroutine call, triggered by an external event.

## Slide 10: Device Status Register
When a device goes “ready” and its IE bit is set, it will generate an interrupt signal
There are several more steps that must allow the interrupt signal to pass before the microsequencer can see it
rdy
IE
Ready Bit
Interrupt Enable Bit
Interrupt

## Slide 11: Interrupt Circuitry, for Completeness
When a device (or devices) interrupts, the priority encoder outputs the highest priority with an interrupt signal
If the priority is greater than the priority in the PL register, the comparator asserts the INT signal to the microsequencer
The new priority is stored in PL
The interrupting device ID is stored in the INTV register (circuit not shown)

## Slide 12: Detecting Interrupts
When the I/O device is allowed to signal an interrupt, the INT control signal to the microcode FSM is asserted
The first state in the FETCH cycle tests to see if INT is asserted
If it is, the microcode transfers to state 49 and sets up a call to the interrupt service routine

## Slide 13: Where to Save Processor State?
Can’t use general purpose registers
  Programmer doesn’t know when interrupt might occur, so she can’t prepare by saving critical registers.
  When resuming, need to restore state exactly as it was.
Can’t use memory allocated by service routine
  Must save state before invoking routine, so the hardware wouldn’t know where.
  Also, interrupts may be nested – that is, an interrupt service routine might also get interrupted!
Use the existing supervisor stack!
  Top of the stack is already known in R6.
  Push state to save, pop to restore.

## Slide 14: Supervisor Stack, for Completeness
Interrupts are handled on the supervisor-mode stack to protect them from user mode programs
  R6 points to the supervisor-mode stack when the PSR is set to Supervisor mode (bit 15) and to the user-mode stack when it’s not
We want to use R6 as stack pointer.
  So that our PUSH/POP routines still work.
When swapping between modes
  Supervisor Stack Pointer (SSP) is saved in Saved.SSP.
  User Stack Pointer (USP) is saved in Saved.USP.
An interrupt in User mode will switch to Supervisor mode, save R6 to Saved.USP, and load R6 from Saved.SSP.

## Slide 15: What is the Processor State?
What three items are needed to completely capture the state of a running process on the LC-3?
(1) Processor Status Register
  Privilege [15], Priority Level [10:8], Condition Codes [2:0]
  This register doesn’t really exist, but the hardware pushes the values on the stack using the following format
(2) Program Counter
  Pointer to next instruction to be executed.
(3) General Registers
  All temporary state of the process that’s not stored in memory.
Privilege (P) has only two values, 0 and 1, but a lot of synonyms.
  1 is user mode or unprivileged mode
  0 is system, supervisor, kernel, or privileged mode

## Slide 16: Handling an Interrupt
Set Table to x01, Vector to INTV (i.e., interrupting device ID)
If PSR[15] == 1 (user state), Saved.USP = R6, R6 = Saved.SSP.
Push PSR and PC-1 to Supervisor Stack.
Set PSR[15] = 0 (supervisor mode).
Set PSR[10:8] = priority of interrupt being serviced.
Set MAR = Table’Vector, where Vector = 8-bit interrupt vector provided by interrupting device (e.g., keyboard = x80).
Load memory location (M[Table’Vector]) into MDR.
Set PC = MDR; now first instruction of ISR will be fetched next.
Go back to the first state of FETCH (state 18)

## Slide 17: Returning from Interrupt
Special instruction – RTI – that restores state.
Pop PC from supervisor stack. (PC = M[R6]; R6 = R6 + 1)
Pop PSR from supervisor stack. (PSR = M[R6]; R6 = R6 + 1)
If PSR[15] = 1, Saved.SSP = R6, R6 = Saved.USP. (If going back to user mode, need to restore User Stack Pointer.)
RTI is a privileged instruction.
  Can only be executed in Supervisor Mode.
  If executed in User Mode, causes an exception. (More about that later.)

## Slide 18: Returning from an Interrupt (RTI)
Special instruction – RTI – that restores state.
Pop PC from supervisor stack. (PC = M[R6]; R6 = R6 + 1)
Pop PSR from supervisor stack. (PSR = M[R6]; R6 = R6 + 1)
If PSR[15] = 1, Saved.SSP = R6, R6 = Saved.USP. (i.e., if going back to user mode, restore User Stack Pointer.)
RTI is a privileged instruction.
  Can only be executed in Supervisor Mode.
  If executed in User Mode, causes an exception. (More about that later.)

## Slide 19: Example (1)
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
x3007
PC
Program A
ADD
x3006
Fetching ADD at location x3006 when Device B interrupts; PC already incremented.
Saved.SSP

## Slide 20: Example (2)
/ / / / / /
x3006
PSR for A
/ / / / / /
/ / / / / /
x2200
PC
R6
Program A
ADD
x3006
Saved.USP = R6. R6 = Saved.SSP.
Push PSR and PC onto stack, then transfer to Device B service routine (at x2200).
x2200
ISR for Device B
x2210
RTI

## Slide 21: Example (3)
/ / / / / /
x3006
PSR for A
/ / / / / /
/ / / / / /
x2203
PC
R6
Program A
ADD
x3006
Executing AND at x2202 when Device C interrupts.
x2200
ISR for Device B
AND
x2202
x2210
RTI

## Slide 22: Example (4)
/ / / / / /
x3006
PSR for A
x2202
PSR for B
x2300
PC
R6
Program A
ADD
x3006
x2200
ISR for Device B
AND
x2202
ISR for Device C
Push PSR and PC onto stack, then transfer to Device C service routine (at x2300).
x2300
x2315
RTI
x2210
RTI

## Slide 23: Example (5)
/ / / / / /
x3006
PSR for A
x2202
PSR for B
x2203
PC
R6
Program A
ADD
x3006
x2200
ISR for Device B
AND
x2202
ISR for Device C
Execute RTI at x2315; pop PC and PSR from stack.
x2300
x2315
RTI
x2210
RTI

## Slide 24: Example (6)
/ / / / / /
x3006
PSR for A
x2202
PSR for B
x3007
PC
Program A
ADD
x3006
x2200
ISR for Device B
AND
x2202
ISR for Device C
Execute RTI at x2210; pop PSR and PC from stack. Restore R6. Continue Program A as if nothing happened.
x2300
x2315
RTI
x2210
RTI
Saved.SSP

## Slide 25
Big deal: Note the microcode is never interrupted; it takes a programmed branch in FETCH1 at the INT signal to save state and change the PC, so it appears the machine instructions have been interrupted!
Stops the microsequencer and transfers control to the interrupt sequencer FSM
Interrupts the microcode, saves all data path registers into a duplicate set of registers, transfers control to the interrupt handler (ISR) address in the interrupt vector table, and on return restores all data path registers before resuming at the interrupted microsequencer state
Waits until the microsequencer reaches the first FETCH state to branch to interrupt-handling microcode which saves the user-visible state on the system stack, changes the PC to point to the interrupt handler (ISR), and branches back to the first FETCH state
Something else
An interrupt signal on the LC-3
10

## Slide 26: Operating Systems?
Most of this we’ll save for CS 2200, but...
Just how are we going to ask the Operating System to do things for us?
Turns out that something like a subroutine call would work, but...
We don’t know where the operating system will be stored in memory (or at least we don’t know where the service procedure we want is stored) and we only have user-mode privileges
So how can we call it?
We’ll use a special instruction, TRAP
  It will jump indirectly through a table provided by the operating system
  It will elevate our privileges to supervisor mode

## Slide 27: TRAP vs JSR(R)
TRAP
  Uses trap vector table
    (Can call from anywhere)
    (TV table is loaded by the OS)
  Normally calls system functions
    I/O, resource sharing, etc.
  Written very carefully!
  If in user state, switch to supervisor state to allow privileged action
JSR(R)
  Nearby (JSR)
  Anywhere (JSRR)
    with some work
  Routine abstraction
  Code reuse/libraries
  No protection mechanism

## Slide 28: LC-3 TRAP Mechanism
1. A set of service routines.
  They are part of operating system – service routines start at arbitrary addresses within the OS (convention is that system code lives between x0200 and x3000)
  Supports up to 256 service routines
2. Using a table of starting addresses.
  Stored at x0000 through x00FF in memory
  Called System Control Block in some architectures
  Initialized by the operating system
3. TRAP instruction.
  Used by program to transfer control to an operating system routine
  8-bit trap vector names one of the 256 service routines
  Saves PSR and PC on via the R6 stack and gains privilege just like Interrupts

## Slide 29: TRAP Instruction
Trap vector
  identifies the address of the system call to invoke
  8-bit index into Trap Vector Table
    in LC-3, this table is stored in memory at 0x0000 – 0x00FF
    8-bit trap vector is zero-extended into 16-bit memory address

## Slide 30: LC-3 Trap
That’s a lot of words! What do they mean!
Think of TRAP as a special indirect JSR with a choice of memory location from 0 through 255 (i.e. let’s call that trapvect).
The TRAP instruction saves state just like an Interrupt on the system stack

## Slide 31: The Trap Vector Table
Trap Vector Table
HALT
subroutine
OUT
subroutine
IN
subroutine
x0420
x04A0
x0520

## Slide 32: Calling the OUT Subroutine with TRAP

## Slide 33: Executing a TRAP Instruction
Zero extend trapvect8 to 16 bits and load into MAR
Read memory into MDR
R7  PC (The Linkage)
PC  MDR
1111
0000
trapvect8
TRAP

## Slide 34: Common LC-3 Trap Numbers
1111
0000
trapvect8
TRAP
Vector | Routine
x23 | IN – prompt and read a character from the keyboard (R0)
x21 | OUT - output a character to the monitor (R0)
x25 | HALT - halt the program
x20 | GETC - read a character from the keyboard (R0)
x22 | PUTS - output a string, 1 char per word ending with x0000, address in R0
x24 | PUTSP - output a string, 2 characters per word ending with a word of x0000, address in R0
See Table A.2 p 543

## Slide 35: Question???
Nothing, the processor will stop when it runs out of instructions
A memory boundary trap will occur
The processor will start to execute the data in memory words following our program
Zombies will come after you!
What happens if there is no HALT instruction in our program?
20

## Slide 36: Stopping the Clock
The LC-3 FSM will repeat its instruction processing sequence as long as the clock is running.
  If not processing instructions from your application, then it is processing instructions from the Operating System (OS) or running off into memory executing whatever is there.
  No sense wasting a scarce opcode for HALT when we can use a trap routine in the OS that resets the RUN register to 0.
To stop the computer:
  AND the clock generator signal with bit 15 of the MCR (machine control register), memory-mapped to 0xFFFE
  When the FSM stops seeing the CLOCK signal change, it stops processing.
(bit 15 in MCR, 0xFFFE)

## Slide 37: Trap Service Routines
The assembler will recognize aliases for certain predefined trap instructions
  TRAP x20 GETC
  TRAP x21 OUT
  TRAP x22 PUTS
  TRAP x23 IN
  TRAP x24 PUTSP
  TRAP x25 HALT

## Slide 38: HOW DO WE GET BACK?

## Slide 39: Compare & Contrast
1100
000
BaseR
000000
JMP
1100
RET
000
111
000000

## Slide 40: Saving & Restoring Registers
Why should we save a register?
When should we save a register?
Who should save the register?
3

## Slide 41: Memory Map of the LC-3

## Slide 42: Exceptions
Now that we understand Interrupts and TRAPs, Exceptions are easy
Synchronous exceptions in the LC-3
  Divide by zero (no divide in LC-3)
  Illegal instruction (opcode=D, Table’Vector is 0x0101)
  Privileged instruction (RTI in user mode, Table’Vector is 0x0100)
  Address Violation (ACV, Table’Vector is 0x0102)
Asynchronous exceptions (not implemented on LC-3)
  Processor error
  Memory error
Handled like Interrupts, but of course the vectors point to exception service routines in the operating system

## Slide 43: Program Discontinuity Logic, for Completeness (Fig C.8)

## Slide 44: Questions?