## Slide 1: Introduction to GBA

## Slide 2: Outline
Why GBA?
Von Neumann Components
  Processor/Control
  Memory
  Input
  Output
Other Goodies
Programming the GBA

## Slide 3: Why GBA?
Programming on bare metal
No operating system
Makes C seem more obvious
Relatively simple hardware
Slow...understand performance tradeoffs
Fun!

## Slide 4: Functional Diagram
Memory
Processor
DMA
Button
Controller
Video
Controller
Audio
Controller

## Slide 5: Functional Diagram
Memory
Processor
DMA
Button
Controller
Video
Controller
Audio
Controller
Video
Display

## Slide 6: Processor
ARM-7-TDMI 3 stage pipelined RISC processor
Very popular embedded processor in 2000-2001
16.78 MHz clock speed
Datatypes
  8 bit (char)
  16 bit (short)
  32 bit (int)
32 bit address space

## Slide 7: ARM-7
Large register file (31 registers/16 at a time)
  Link register
  Program Counter
Load/store architecture
Fixed length instructions
6 Modes (User + 5 types of exceptions)
Status register (Neg, Zero, Carry, Overflow)
Two instruction sets!

## Slide 8: ARM 7 Processor Apps
Audio processing in the SEGA Dreamcast
D-Link DSL-604+ Wireless ADSL Router[2]
iPod from Apple
iriver portable digital audio players (the H10 uses a chip with this processor)
Juice Box
Lego Mindstorms NXT
Most of Nokia's mobile phone range.
Nintendo DS (co-processor) and Game Boy Advance from Nintendo
PocketStation
Roomba 500 series from iRobot
Sirius Satellite Radio receivers
The main CPU in Stern Pinball S.A.M System games.
Many automobiles embed ARM7 cores.

## Slide 9: Memory
RAM
  Random Access Memory
ROM
  Read Only Memory
ROM is RAM but not all RAM is ROM
Volatile
Persistent

## Slide 10: Recall
0x1 = 1
0x10 = 16
0x100 = 256
0x1000 = 4,096
0x1 0000 = 65,536
0x10 0000 = 1,048,576 (1 M)
0x100 0000 = 16,777,216 (16 M)
0x1000 0000 = 268,435,456 (256 M)
0x1 0000 0000 = 4,294,967,296 (4 G)

## Slide 11: System ROM
You can't get to it!
00000000-00003FFFF
System ROM
16KB
02000000-0203FFFF
EXRAM
256KB
03000000-03007FFF
IWRAM
32KB
04000000
Hardware Registers
05000000-050003FFF
Palette Memory
1KB
06000000-06017FFF
Video RAM
96KB
07000000-070003FF
Object Attribute Memory
1 KB
0800000
Game Pak ROM
Wait State 0
255 Mbits (~32Mb)
0A00000
Game Pak ROM
Wait State 1
255 Mbits (~32Mb)
09FE0000
Game Pak Flash
Wait State 0
1Mbit(128KB)

## Slide 12: WRAM
Internal Working RAM
Sometimes called Working RAM
On the ARM chip
Very fast
Costly
Globals, static, stack all go here by default!
Force functions?
0x03 000 000
00000000-00003FFFF
System ROM
16KB
02000000-0203FFFF
EXRAM
256KB
03000000-03007FFF
IWRAM
32KB
04000000
Hardware Registers
05000000-050003FFF
Palette Memory
1KB
06000000-06017FFF
Video RAM
96KB
07000000-070003FF
Object Attribute Memory
1 KB
0800000
Game Pak ROM
Wait State 0
255 Mbits (~32Mb)
0A00000
Game Pak ROM
Wait State 1
255 Mbits (~32Mb)
09FE0000
Game Pak Flash
Wait State 0
1Mbit(128KB)

## Slide 13: Memory Tradeoff
COST
Speed

## Slide 14: EXRAM
External RAM
Heap (malloc)
Can force variables here
00000000-00003FFFF
System ROM
16KB
02000000-0203FFFF
EXRAM
256KB
03000000-03007FFF
IWRAM
32KB
04000000
Hardware Registers
05000000-050003FFF
Palette Memory
1KB
06000000-06017FFF
Video RAM
96KB
07000000-070003FF
Object Attribute Memory
1 KB
0800000
Game Pak ROM
Wait State 0
255 Mbits (~32Mb)
0A00000
Game Pak ROM
Wait State 1
255 Mbits (~32Mb)
09FE0000
Game Pak Flash
Wait State 0
1Mbit(128KB)

## Slide 15: Video&Hardware
Hardware Registers
  Sound
  DMA
  etc.
Palette RAM
Video RAM
Oject Attribute Memory
00000000-00003FFFF
System ROM
16KB
02000000-0203FFFF
EXRAM
256KB
03000000-03007FFF
IWRAM
32KB
04000000
Hardware Registers
05000000-050003FFF
Palette Memory
1KB
06000000-06017FFF
Video RAM
96KB
07000000-070003FF
Object Attribute Memory
1 KB
0800000
Game Pak ROM
Wait State 0
255 Mbits (~32Mb)
0A00000
Game Pak ROM
Wait State 1
255 Mbits (~32Mb)
09FE0000
Game Pak Flash
Wait State 0
1Mbit(128KB)

## Slide 16: Game Pak ROM
Cartridge Memory
Making an array const will put it here.
Code goes here
  main
  functions
00000000-00003FFFF
System ROM
16KB
02000000-0203FFFF
EXRAM
256KB
03000000-03007FFF
IWRAM
32KB
04000000
Hardware Registers
05000000-050003FFF
Palette Memory
1KB
06000000-06017FFF
Video RAM
96KB
07000000-070003FF
Object Attribute Memory
1 KB
0800000
Game Pak ROM
Wait State 0
255 Mbits (~32Mb)
0A00000
Game Pak ROM
Wait State 1
255 Mbits (~32Mb)
09FE0000
Game Pak Flash
Wait State 0
1Mbit(128KB)

## Slide 17: Game Pak Flash
Cartridge Memory
Can write to this block
Could store or use sprintf, etc.
00000000-00003FFFF
System ROM
16KB
02000000-0203FFFF
EXRAM
256KB
03000000-03007FFF
IWRAM
32KB
04000000
Hardware Registers
05000000-050003FFF
Palette Memory
1KB
06000000-06017FFF
Video RAM
96KB
07000000-070003FF
Object Attribute Memory
1 KB
0800000
Game Pak ROM
Wait State 0
255 Mbits (~32Mb)
0A00000
Game Pak ROM
Wait State 1
255 Mbits (~32Mb)
09FE0000
Game Pak Flash
Wait State 0
1Mbit(128KB)

## Slide 18: Typical GBA Memory Map
00000000-00003FFFF
System ROM
16KB
02000000-0203FFFF
EXRAM
256KB
03000000-03007FFF
IWRAM
32KB
04000000
Hardware Registers
05000000-050003FFF
Palette Memory
1KB
06000000-06017FFF
Video RAM
96KB
07000000-070003FF
Object Attribute Memory
1 KB
0800000
Game Pak ROM
Wait State 0
255 Mbits (~32Mb)
0E000000
Game Pak Flash
Wait State 0
1Mbit(128KB)
For your information…
RAM; 16-bit path to memory
RAM; 32-bit path to memory
Device registers: Audio, video control, DMA, etc.
Color map, video buffer, sprites
Game cartridge ROM
Game cartridge nonvolatile RAM

## Slide 19: Question
8 bits
16 bits
32 bits
64 bits
10
How big is a short on the GBA?

## Slide 20: Input
10 buttons
  Start
  Select
  A
  B
  Left
  Right
  Up
  Down
  Left shoulder
  Right shoulder

## Slide 21: Input
One button register
1 bit per button
  0 pressed
  1 not pressed

## Slide 22: Output
240 x 160 pixel color video display screen
6 display modes
  Bit mapped
  Tiled
Hardware support for sprites
Video Memory
Video
Controller
Display

## Slide 23: Output
Sound effect generators
Direct Sound Hardware (DAC)

## Slide 24: Other Goodies
Interrupts
Timers
DMA

## Slide 25: Programming
Download and install the software from Canvas (part of the Docker container you already have)
Download tutorials
  http://www.coranac.com/tonc/text/
  (Mode 3 and DMA, sections 5 and 14)
etc.

## Slide 26: Two Potential Problems w/Macros
#define SQUARE(X) (X * X)
int z = SQUARE(2);
int z = SQUARE(x + y);
Fix:
#define SQUARE(X) ((X) * (X))
Cuddling – don’t leave
a space here!
Suppose you have Square(2 + 3)
Using the macro above, the text substitution yields: (2 + 3 * 2 + 3)
And, due to the algebraic order of operations, this gives 11
Again, suppose you have Square(2 + 3). Now, with the new macro, the text substitution yields: ((2 + 3) * (2 + 3))And, with the algebraic order of operations, this gives 25

## Slide 27: Light Up a Pixel

## Slide 28: Datatypes on the GBA
Integers
  (All can be signed, the default, or unsigned)
  char (1 byte)
  short int OR short (2 bytes)
  int (4 bytes)
  long int OR long (8 bytes)
Floating Point
  (To be avoided because they’re software emulated)
  Float
  double

## Slide 29: Old Friends?
Remember our friends, the device registers?
GBA has quite a few
One register controls the many video modes on the GBA
REG_DISPCTL is at 0x0400 0000
And by the way, how do we touch that device register in C?
*(unsigned short *)0x04000000
or better yet #define REG_DISPCTL (*(unsigned short *)0x04000000)
We’ll be using Mode 3 and BG2 for our programming!

## Slide 30: REG_DISPCTL
Bits 0-2 Mode
  0,1,2 Tile Modes
  3, 4, 5 Bitmap Modes
For bitmapped graphics use BG2
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
0F
0E
0D
0C
0B
0A
09
08
07
06
05
04
03
02
01
00
Mode
BG0
BG1
BG2
BG3

## Slide 31: REG_DISPCTL
Bits 0-2 Mode
  0,1,2 Tile Modes
  3, 4, 5 Bitmap Modes
For bitmapped graphics use BG2
100 0000 00112 = 0x403
100000000112 = 210 + 21 + 20 = 1024 + 2 + 1 = 1027
REG_DISPCTL = 0x403;
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
0F
0E
0D
0C
0B
0A
09
08
07
06
05
04
03
02
01
00
Mode
BG0
BG1
BG2
BG3

## Slide 32: Video Memory (in Mode 3)
Starts at 0x0600 0000
Consists of 160 x 240 16-bit unsigned shorts
Rows are assigned contiguously, one after the next
How can we access this memory from C, starting at this address?
What is the address of the pixel at
  Row 5
  Column 8

## Slide 33: Video Memory
How do we get to the pixel at row 5, col 8?
What does this question remind you of?
240
X [5,8]
160

## Slide 34: Video Memory
Looks like a two-dimensional array stored in row major order, right?
So how do we calculate an offset from the beginning?
240
X [5,8]
160

## Slide 35: Video Memory
How about row * cols + col, i.e. offset = 5 * 240 + 8 offset = 1208
160
240
X [5,8]

## Slide 36: Video Memory
Now that we know the offset into the array, just add the base offset = 5 * 240 + 8; *((unsigned short *)0x6000000 + offset)
160
240
X [5,8]

## Slide 37: And What Does a Pixel Look Like?
Video Memory (in Mode 3, which is all we’ll talk about)
How do we control the color?
What would white be?
  In Hex
  In Decimal
0x7fff = 32767
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 38: Question
offset = 29 * 240 + 80
offset = 80 * 160 + 29
offset = 80 * 240 + 29
offset = 29 * 160 + 80
How would we calculate the offset of the pixel at row 29, column 80?
20
Today’s number is 68,068

## Slide 39: Question
Red
Blue
Green
Yellow
Magenta
What color does 0x3E0 represent on the GBA?
0
0
0
0
0
0
1
1
1
1
1
0
0
0
0
0
0
3
E
0
30
Click to add text

## Slide 40: So How Do We Set That Pixel?
We know the base of video memory is 0x0600000, so unsigned short *videoBuffer = (unsigned short *)0x0600000; videoBuffer[5*240+8] = 0x7fff;
Could we also say *(videoBuffer + 5*240+8) = 32767;

## Slide 41: How Might We Do This in LC-3 Assembly?
We have to make the assumption that LC-3 has 32-bit memory and registers, but byte addressing like the ARM
; unsigned short *videoBuffer = (unsigned short *)0x06000000; LD R0,VBADDR ST R0,videoBuffer ; videoBuffer[5*240+8] = 0x7fff; LD R0,videoBuffer LD R1,offset ADD R1,R1,R1 ;; because a short is 2 bytes ADD R0,R0,R1 ;; pixel address is now in R0 LD R1,WHITE STR R1,R0,#0 HALT WHITE .fill 0x7fff VBADDR .fill 0x06000000 videoBuffer .fill 0 offset .fill 1208 ; 5*240+8

## Slide 42: What About ARM Assembly?
@ unsigned short *videoBuffer = 0x6000000;
﻿videoBuffer: .word 0x6000000
...
@ videoBuffer[5*240+8] = 0x7fff;
ldr r1, .L3 @ Load addr of VideoBuffer
ldr r3, [r3] @ Load contents (like LDI!) ldr r2, #2416 @ r2 = 2416
add r3, r3, r2 @ r3 = r3 + r2
ldr r2, .L4 @ load 0x7fff into r2
strh r2, [r3] @ store halfword [like STI!]
...
.align 2
.L3: .word videoBuffer
.L4: .word 0x7fff

## Slide 43: Pointers
Address Variables
  Variables that contain the address of other variables
Strange and beautiful syntax
  Declaring a pointer variable
  Using a pointer variable
    Storing a value in the pointer
    Storing a value in the variable being pointed to by the pointer

## Slide 44: Pointers
Putting an address into a variable
.orig x3000
LD R1 val
ST R1 ptr
HALT
val .fill x4000000
ptr .fill 0
unsigned short *ptr;
ptr = (unsigned short *)0x4000000;
Putting a value into the location contained in a pointer
.orig x3000
LD R1 ptr
LD R2 var
STR R2 R1 0
HALT
ptr .fill x4000000
var .fill 1027
LD R2 var
STI R2 addr

## Slide 45: Pointers
.orig x3000
LD R1, Value
STI R1, Dispctla
Dispctla .fill 0x4000000
Value .fill 1027

## Slide 46: C
unsigned short *ptr;
ptr = 0x4000000;
unsigned short *ptr;
ptr = 0x4000000;
*ptr = 1027;
The * operator has two meanings when used in conjunction with pointers i.e. not as the multiplication binary operator:
Used to declare a variable as a pointer (where
we must tell C what we are pointing at.
Used to dereference a pointer (i.e. We are
referring to what the pointer is pointing to as
opposed to the value of the pointer)

## Slide 47: Nota Bene
unsigned short *ptr = 0x4000000;
Same as
unsigned short *ptr;
ptr = 0x4000000;

## Slide 48: Let's Light Up a Pixel
int main(void)
{
*(unsigned short *)0x4000000 = 1027;
*(unsigned short *)0x60096F0 = 32767;
while(1)
{
}
return 0;
}

## Slide 49: Let's Light Up a Pixel
#define REG_DISPCTL *(unsigned short *)0x4000000
unsigned short *pixelAddress;
int main(void)
{
pixelAddress = 0x60096F0;
REG_DISPCTL = 1027;
*pixelAddress = 32767;
while(1)
{
}
return 0;
}

## Slide 50: Let's Light Up a Pixel
#define REG_DISPCTL *(unsigned short *)0x4000000
unsigned short *pixelAddress =
(unsigned short *) 0x60096F0;
int main(void)
{
REG_DISPCTL = 1027;
*pixelAddress = 32767;
while(1)
{
}
return 0;
}

## Slide 51: Let's Light Up a Pixel
#define REG_DISPCTL *(unsigned short *)0x4000000
unsigned short *pixelAddress =
(unsigned short *) 0x60096F0; int main(void)
{
REG_DISPCTL = 1027;
*pixelAddress = 0x7FFF;
while(1)
{
}
return 0;
}

## Slide 52: Let's Light Up a Pixel
#define REG_DISPCTL *(unsigned short *)0x4000000
unsigned short *pixelAddress =
(unsigned short *) 0x60096F0; int main(void)
{
REG_DISPCTL = 1027;
*pixelAddress = 0x7FFF;
while(1)
{
}
return 0;
}
Why two different ways of handling addresses?

## Slide 53: Let's Light Up a Pixel
#define REG_DISPCTL *(unsigned short *)0x4000000
unsigned short *pixelAddress =
(unsigned short *) 0x60096F0; int main(void)
{
REG_DISPCTL = 1027;
*pixelAddress = 0x7FFF;
pixelAddress++;
*pixelAddress = 0x1F;
*(++pixelAddress) = 0x1F<<5;
*(++pixelAddress) = 0x1F<<10;
while(1) {}
return 0;
}

## Slide 54
#define RGB(r,g,b) ((r)|((g)<<5)|((b)<<10))
#define WHITE RGB(31,31,31)
#define RED(31,0,0)
#define GREEN RGB(0,31,0)
#define BLUE RGB(0,0,31)
#define REG_DISPCTL *(unsigned short *)0x4000000
unsigned short *pixelAddress =
(unsigned short *) 0x60096F0; int main(void) {
REG_DISPCTL = 1027;
*pixelAddress = WHITE;
pixelAddress++;
*pixelAddress = RED;
*(++pixelAddress) = GREEN;
*(++pixelAddress) = BLUE;
while(1) {}
return 0;
}

## Slide 55: Can the fun ever stop?

## Slide 56
#define RGB(r,g,b) ((r)|((g)<<5)|((b)<<10))
#define OFFSET(row,col) ((row)*240+(col))
#define WHITE RGB(31,31,31)
#define RED(31,0,0)
#define GREEN RGB(0,31,0)
#define BLUE RGB(0,0,31)
#define REG_DISPCTL *(unsigned short *)0x4000000
unsigned short *videoBuffer =
(unsigned short *)0x6000000;
int main(void) {
REG_DISPCTL = 1027;
videoBuffer[OFFSET(80,160)] = WHITE;
videoBuffer[OFFSET(80,161)] = RED;
videoBuffer[OFFSET(80,162)] = GREEN;
videoBuffer[OFFSET(80,163)] = BLUE;
while(1) {}
return 0;
}

## Slide 57: Put (almost) all this in a header file!
// myLib.h
#define RGB(r,g,b) ((r)|((g)<<5)|((b)<<10))
#define OFFSET(row,col) ((row)*240+(col))
#define WHITE RGB(31,31,31)
#define RED(31,0,0)
#define GREEN RGB(0,31,0)
#define BLUE RGB(0,0,31)
#define REG_DISPCTL *(unsigned short *)0x4000000
unsigned short *videoBuffer =
(unsigned short *)0x6000000;

## Slide 58: Put all this in a header and a library file!
// myLib.h
#define RGB(r,g,b) ((r)|((g)<<5)|((b)<<10))
#define OFFSET(row,col) ((row)*240+(col))
#define WHITE RGB(31,31,31)
#define RED(31,0,0)
#define GREEN RGB(0,31,0)
#define BLUE RGB(0,0,31)
#define REG_DISPCTL *(unsigned short *)0x4000000
extern unsigned short *videoBuffer;
//mylib.c
unsigned short *videoBuffer =
(unsigned short *)0x6000000;

## Slide 59
#include "myLib.h"
int main(void) {
REG_DISPCTL = 1027;
videoBuffer[OFFSET(80,160)] = WHITE;
videoBuffer[OFFSET(80,161)] = RED;
videoBuffer[OFFSET(80,162)] = GREEN;
videoBuffer[OFFSET(80,163)] = BLUE;
while(1) {}
return 0;
}

## Slide 60: Making Things Clear(er)

## Slide 61
// myLib.h
#define RGB(r,g,b) ((r)|((g)<<5)|((b)<<10))
#define OFFSET(row,col) ((row)*240+(col))
#define SETMODE(mode) REG_DISPCTL = (mode)
#define WHITE RGB(31,31,31)
#define RED(31,0,0)
#define GREEN RGB(0,31,0)
#define BLUE RGB(0,0,31)
#define REG_DISPCTL *(unsigned short *)0x4000000
#define BG2_ENABLE 0x400
#define MODE3 3
extern unsigned short *videoBuffer;
//mylib.c
unsigned short *videoBuffer =
(unsigned short *)0x6000000;

## Slide 62: REG_DISPCNT
Bits 0-2 Mode
  0,1,2 Tile Modes
  3, 4, 5 Bitmap Modes
For bitmapped graphics use BG2
100 0000 00112 = 0x403
100000000112 = 210 + 21 + 20 = 1024 + 2 + 1 = 1027
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
0F
0E
0D
0C
0B
0A
09
08
07
06
05
04
03
02
01
00
Mode
BG0
BG1
BG2
BG3

## Slide 63
#include "myLib.h"
int main(void) {
SETMODE(BG2_ENABLE | MODE3);
videoBuffer[OFFSET(80,160)] = WHITE;
videoBuffer[OFFSET(80,161)] = RED;
videoBuffer[OFFSET(80,162)] = GREEN;
videoBuffer[OFFSET(80,163)] = BLUE;
while(1) {}
return 0;
}

## Slide 64: Questions?