## Slide 1: GBA C Programming

## Slide 2: Quick Overview

## Slide 3: Functional Diagram
Memory
Processor
DMA
Button
Controller
Video
Controller
Audio
Controller
Video
Display

## Slide 4: Blanking Intervals

## Slide 5: Cathode Ray Tube

## Slide 6: Color CRT
Note that in real life, the beams are not colored. Red, blue and green electrons are a myth. It’s the phosphors on the screen that glow in colors!

## Slide 7: NTSC Scanning Pattern (interleaved)
http://belogic.com/uzebox/video_primer.htm

## Slide 8: Blanking
GBA screen is refreshed at 60 Hz
There are pauses in the drawing process
  For each scanline (160 lines)
    Draw scanline (240 pixels)
    Hblank (68 pixels)
  Vblank (68 scanlines)
To avoid tearing, positional data is usually updated at the VBlank. This is why most games run at 60 or 30 fps.
FYI, this mimics the NTSC/PAL analog TV standards which required blanking intervals to reposition the electron beam.

## Slide 9: HBlank and VBlank

## Slide 10: Drawing Times
A full screen refresh takes exactly 280896 cycles, divided by the clock speed gives a frame rate of 59.73.
From the Draw/Blank periods given above you can see that there are 4 cycles per pixel, and 1232 cycles per scanline.

## Slide 11
Video
Controller
Video
Display
videoBuffer
Video
Controller
Video
Display
videoBuffer
Video
Controller
Video
Display
videoBuffer
during vblank: make changes to the videoBuffer
1
during vdraw: perform other useful computations
2
during vblank: make changes to the videoBuffer
1
during vblank: make changes to the videoBuffer
1
during vdraw: perform other useful computations
2
during vdraw: perform other useful computations
2
Time ->

## Slide 12: Processing Pipeline
Video
Controller
Video
Display
videoBuffer
Video
Controller
Video
Display
videoBuffer
during vblank: make changes to the videoBuffer
1
during vdraw: perform other useful computations
2
balls[], oldballs[] and other data
Memory
drawRect()
during vblank: make changes to the videoBuffer
1
during vdraw: perform (lots of) other useful computations
2

## Slide 13: Question
60
64
68
72
160
10
How many scan line times are available during the vertical blanking interval on the GBA?

## Slide 14: Button Input

## Slide 15: Input
10 buttons (bit 0 through bit 9 of button register)s
  A
  B
  Start
  Select
  Right
  Left
  Up
  Down
  Right shoulder
  Left shoulder

## Slide 16: Input
One button register
1 bit per button
  0 pressed
  1 not pressed

## Slide 17: Definitions
#define BUTTONS *(volatile
unsigned int *)0x4000130
#define KEY_DOWN_NOW(key)
(~(BUTTONS) & key)

## Slide 18: Question
Executing a special I/O instruction
Reading from a device register
Reading a word from memory
Loading the button register into a general purpose register
The positions of the GBA’s ten buttons can be discovered programmatically by

## Slide 19: Multiple Code Files

## Slide 20: Conventions
Files ending in .h
  Declarations (no storage allocation)
  Macros (#define)
  Function prototypes
  Can only #include other .h files
Files ending in .c
  Definitions (allocation of storage)
  Functions
  Can only #include .h files
  .c files are never included by anyone else

## Slide 21: Configuration
// Library file
#include "Header.h"
int blah = 42;
void whee()
{
// Code
}
// Program files
// Program files
// Program files
// Program files
#include "Header.h"
int main()
{
whee();
...
// Header.h
typedefs
#defines
extern int blah;
void whee();

## Slide 22: Example
video.c contains
  reusable video functions
  Variable definitions e.g.
    unsigned short *videoBuffer =
    (unsigned short *)0x6000000;
  #include video.h

## Slide 23: Example
video.h contains
  typedefs
  #defines
  extern unsigned short *videoBuffer;
  prototypes for functions found in video.c

## Slide 24: Example
All program files containing functions that use any of the functions in video.c should include video.h; video.c should be included in the project makefile

## Slide 25: DMA

## Slide 26: What is DMA?
DMA = Direct Memory Access
Hardware supported data copy
  Up to 10x as fast as array copies
  You set it up, the CPU is halted, data is transferred, and CPU gains back control
    Careful—reckless use can block interrupts

## Slide 27: DMA Channels
Channel 0
  Highest Priority
  Time Critical Operations
  Only works with IWRAM
Channel 1 & 2
Transfer sound chunks to sound buffer
Channel 3
  Lowest Priority
  General purpose copies, like loading tiles or bitmaps into memory

## Slide 28: Using DMA
Source
  REG_DMAxSAD (x = 0, 1, 2, 3)
  The location of the data that will be copied
Destination
  REG_DMAxDAD
  Where to copy the data to
Amount
  REG_DMAxCNT (DMA control)
  How much to copy

## Slide 29: REG_DMAxCNT
Lower 16 bits contain amount to transfer
Upper 16 bits contain other options
Turn on a DMA channel
When to perform the DMA
How the copy source and destination behave
How much to copy at a time
Whether or not to throw an interrupt on completion
Repeat or don't repeat on finish
Can be treated as one 32 bit register, or two 16 bit registers

## Slide 30: REG_DMAxCNT
bits name define description
0-15 N Number of transfers.
21-22 DA DMA_DST_INC 00: increment after each transfer
(default)
DMA_DST_DEC 01: decrement after each transfer
DMA_DST_FIXED 10: none; address is fixed
DMA_DST_RESET 11: haven't used it yet, but
apparently this will increment
the destination during the
transfer, and reset it to the
original value when it's done.
23-24 SA DMA_SRC_INC
DMA_SRC_DEC
DMA_SRC_FIXED
Source Adjustment. Works just like the two bits
for the destination. Note that there is no
DMA_SRC_RESET; code 3 for source is forbidden.
25 R DMA_REPEAT Repeats the copy at each VBlank or
HBlank if the DMA timing has been set to
those modes.

## Slide 31: REG_DMAxCNT
bits name define description
26 CS DMA_16,
DMA_32 Chunk Size.
Sets DMA to copy by halfword (if clear) or word (if set).
28-29 TM DMA_NOW 00: start immediately
DMA_AT_VBLANK 01: start at VBlank
DMA_AT_HBLANK 10: start at HBlank.
DMA_AT_REFRESH 11: Never used it so far, but here's how
I gather it works. For DMA1 and DMA2 it'll refill the
FIFO when it has been emptied. Count and size are forced
to 1 and 32bit, respectively. For DMA3 it will start the
copy at the start of each rendering line, but with a 2
scanline delay.
Timing Mode. Specifies when the transfer should start.
30 I DMA_IRQ Interrupt request. Raise an interrupt when
finished.
31 En DMA_ON Enable the DMA transfer for this channel.

## Slide 32: Source Adjustment
REG_DMAxCNT bits 23-24
Incrementing source (default: 002) causes DMA to behave as a memory copy
Fixing source (102) causes DMA to behave as a memory fill
  Copy the same thing over and over to a stretch of memory
  Fill the screen with a color, clear a tilemap to all zeros, etc
    Careful! SAD takes an address, not a value!
    Make local variables volatile if using their address for a DMA fill

## Slide 33: DMA Setup
We map a struct array over the DMA registers
typedef struct {
const volatile void *src;
void *dst;
u32 cnt;
} DMA_CONTROLLER;
#define DMA((volatile DMA_CONTROLLER *)
0x040000b0)

## Slide 34: DMA Setup (cont)
#define DMA_TRANSFER(_dst,_src,_count,_ch,_mode) \
do { \
DMA[_ch].cnt = 0; \
DMA[_ch].src = (const void*)(_src); \
DMA[_ch].dst = (void*)(_dst); \
DMA[_ch].cnt = (_count) | (_mode); \
} while(0)
void dma_memcpy(void *dst, const void *src, u16 count)
{
DMA[3].cnt = 0; // shut off previous transfer
DMA[3].src = src;
DMA[3].dst = dst;
DMA[3].cnt = count | DMA_32| DMA_ON;
}

## Slide 35: DMA Timing
Clearing a DMA register before its scheduled copy occurs will stop it from ever happening
  Careful when using delayed DMA
Even immediate DMA has a 2 cycle delay
  DMA calls in immediate succession could cancel the earlier one
  2 cycles is short enough that returning from the DMA setup function allows the copy to begin before other code executes

## Slide 36: Question
6
8
12
16
20
How many bytes are occupied by a GBA DMA channel’s device registers?
typedef struct {
const volatile void *src; //4
void *dst; //4
u32 cnt; //4
} DMA_CONTROLLER;

## Slide 37: Filling a Rectangle

## Slide 38: Why is DMA so Fast

## Slide 39: Questions?

## Slide 40: Loop Template
Initialize
While true
  Previous state = Current state
  Check buttons
  Calculate new values for Current state
  Wait for Vblank
  Undraw using Previous state
  Draw using Current state

## Slide 41: Loop Template
Set Gamestate to INITPLAY
While true
  Previous state = Current state
  if Gamestate == PLAY
    Check buttons
    Calculate new values for Current state
  Else if Gamestate == INITPLAY
    Initialize the Current state
  Wait for Vblank
  If Gamestate == PLAY
    Undraw using Previous state
    Draw using Current state
  Else if Gamestate == INITPLAY
    Gamestate = PLAY

## Slide 42: Text

## Slide 43: ASCII Table

## Slide 44: fontdata_6x8[]